## Slide 1: ACC
Case Analysis
Slides handed out in class
Notes: Cold call 1: How did your group describe and evaluate the OS of ACC v. DJC?
Cold call 2: How serious is the threat? What analysis has your group done?
Cold call 3: What is your action plan?
Case summary: You have read the ACC case: DJC is rumored to build a replica of its most efficient connector plant at Kawasaki in the US. With the overcapacity and the fact that ACC still has a cost advantage, nobody was really concerned. Now, however, DJC seems serious and Denise Larsen, VP of Ops at ACC, is wondering what to do:
- Jack Mitchell, her assistant, believes ACC should completely overhaul its OS and basically replicate DJC’s before they come in.
- Andy Li, Sunnyvale’s plant manager, sees no need for panic and believes cost-cutting is sufficient given that DJC will not easily replicate its strategy in the US and that its new US plant would be completely different from Kawasaki.
Our goal is to come up with a recommendation to Denise. I suggest the following “AAA” plan (put on BB; or keep one board per A):
Assess the situation by contrasting ACC and DJC’s OS. This is an application of class 1.
  Apply framework: strat (value pos + financial view); competency; resource & process views
  Check alignment: PP matrix! (DJC is aligned while 85% of ACC’s business is not aligned and thus inefficient.)
Analyze the sources of the cost differential.
  Adjust for location + time (learning)
  Volume
  strategy
Assess the threat and recommend a plan of action.
  The larger question is: what to do with the 85%? Do we stick to our knitting (custom)=“retreat”, do both =“fight”, or only standard = “adopt”? (Similar to Swatch and FedEx-UPS. Take poll. Likely to keep standard b/ customer retention model)
  If we do standard, recognize in process (this is basic + see some discussion in later slide)
  So, let us focus on our core market: how serious is threat there, what can we do?
Do all of this w/o slides (only have framework on transparency). After 45min, “let us review a few slides to illustrate the analytics.”

## Slide 2: Diagnostic: Alignment Strategic Operational Audit
Strategy Gap?
Capability Gap?
Assets & Process Gap?
Value
Proposition
Assets
&
Processes
Capabilities
Deliverable
Value
Propositions
Desired
Capabilities
Desired
Assets &
Processes
Market
view
Resource
view
Notes: For ACC, there is misalignment. Key question is: do we adjust strategy (stick to our knitting, move to standard only, or do both) and/or do we adjust operations?

## Slide 3: Diagnostic: Alignment Product-Process Matrix
Jumbled flow
Process segments
loosely linked
Disconnected line flow
Jumbled flow but a
dominant flow exists
Job Shop
Connected line flow
(e.g., assembly line)
Continuous, automated,
rigid line flow
Process segments tightly
linked
(high opportunity costs)
Inefficient
(high out-of-pocket costs)
Infeasible
Flow Shop
Process Technology
(Flexibility)
(Low)
(High)
Product
Concept
(Variety)
(Low)
Customer Solutions
One of a kind
Low volume
Many Products
Few Major Products
Standardized Products
Commodity products
High volume
(High)
Zone of Alignment
A
B
C
D
Notes: Remind them of the misalignment of ACC: wide horizontal strip (15% custom bu 85% standard) is executed through job-shop like process

## Slide 4: How to describe the strategic role of operations? The “Four Stages” classification
Notes: Ask: Where would you put the organization that you worked for?
These “four stages” can be used to:
Identify current position by summarizing the overall role of OS within a company’s competitive strategy.
Judge how long it may take to progress to the next stage
Suggest changes to be made in other parts of the organization to sustain a higher level/stage.
The stages are easiest understood by considering a specific activity in the value chain. (Originally the stages were designed to consider the strategic role of manufacturing!)
I think you should be familiar with these stages, so let’s quickly explain what they mean: Give a company example for each stage:
start-ups, hi-techs driven by mostly by ideas/invention rather than execution
Many market or R&D-driven companies: Traditional steel, auto, pharma, R&D driven!
An outside competitor (such as perhaps from China) may force a stage 2 company to become stage 3.
“Operational excellence”: Toyota, Dell, Walmart.
Note:
Often different drivers (e.g. sourcing v. flexibility) can be at different levels -> this shows which drivers are key to OS! (The entire organization’s stage can be thought of as “where the center of gravity is”.)
  BioPharma: Theravance believes they are stage 4 in “operations”, by which they mean integrating the project flow. Clearly, from a mfg perspective only, they’re lower (they outsource mfg)
It is difficult, if not impossible, to skip a stage.
It is not true that every company should strive for stage 4! That depends on the overall CS. A company like Nordstrom would be foolish to put all its efforts into operations. Rather, each company should decide whether it should be stage 3 or 4. Stages 1 or 2 are not for leaders!

## Slide 5: Assessment of the Threat
The question:
  What would happen if DJC enters and uses its current operating system to produce differentiated products and services (ACC’s niche): would DJC still have a cost advantage?
Steps:
  Assess the situation by contrasting ACC and DJC’s OS.
  Analyze the sources of the cost differential.
  Assess the threat and recommend a plan of action.
Notes: Recall that our goal is to come up with a recommendation to Denise using the following plan:
Assess the situation by contrasting ACC and DJC’s OS. This is an application of class 1. Done
Analyze the sources of the cost differential. Let’s now analyze the cost differential, focusing on ACC’s process for its custom segment b/c that’s the question we’re interested in.
Assess the threat and recommend a plan of action.

## Slide 6: Competitive Cost Analysis
 | DJC/Kawasaki | DJC @ US | DJC @ US, volume | DCS + OE | DCS | DCOE | ACC @ volume | ACC
RM (product + packaging) | $ 14.89 | $ 8.93 |  |  |  |  |  | $ 11.49
DL | $ 3.02 | $ 3.32 |  |  |  |  |  | 
IL | $ 0.75 | $ 0.83 |  |  |  |  |  | 
Total Labor | $ 3.77 | $ 4.15 |  |  |  |  |  | $ 10.30
Electricity | $ 1.40 | $ 1.12 |  |  |  |  |  | $ 0.80
Depreciation | $ 1.80 | $ 1.80 |  |  |  |  |  | $ 5.10
Other | $ 4.24 | $ 4.24 |  |  |  |  |  | $ 6.10
Total | $ 26.10 | $ 20.24 |  |  |  |  |  | $ 33.79
(Dollars per thousand units, 1991) |  |  |  |  |  |  |  | 

## Slide 7: Analyzing the Cost Differential: 1. COGS Line item: Raw Materials
DC RM = (9.39+2.10) – (12.13+2.76) *.60 = $11.49 - $8.94 = $2.55 US-localized
How much is driven by volume?
How much is driven by strategy?
  If DJC were to adopt ACC’s product strategy, its cost would increase by
  Thus, to match ACC product value, DJC’s US-product cost would be $8.94 + $2.45 = $11.39. Thus, the strategic trade-off is DCS, RM = $2.45
The remainder is due to OE: DCOE, RM = $11.49-$11.39= $2.55 - $2.45 = $0.10
Notes: First: localize!
RM is mostly variable cost, so no volume effect.
Estimate how DJCs cost would increase if it were to provide ACC level of product quality, flexibility and responsiveness: it must use gold plating and smaller reel, increasing its cost by $2.45 to $11.39. This is the essential strategic trade-off in RM costs. (Notice that what we call OE depends on the customer segment: for military and aerospace, you probably want the expensive resing and the bigger mass. Sunnyvale serves computers, telecom and scientific instruments. For consumer and regular business, the table is fine. For military and aerospace, you probably put resin and mass into strategy. This reduces DCOE by $.66 and would make it a negative number (-$.56), which would be good news for ACC.)
Thus, the DJC’s cost-advantage after correcting for strategy is $11.49-$11.39=$.10. This means that if DJC were to copy our product strategy, they would still have a $.10 cost advantage.
So what? Addressing the second question: what can ACC do to protect itself? Well, they could improve their costs by $1.92*.60 = $1.15 by adopting the efficiency tricks of DJC without hampering their innovation/quality proposition. Notice that the result would be that then ACC has a cost-advantage over what DJC could do: ACC new RM cost would be $11.49-$1.15=$10.34. Compared to what DJC could do, DJC would now be at a cost disadvantage for RM of $10.34-$11.39=-1.04.
General caveat: We must be careful in interpreting the COGS numbers. These are standard costs; i.e., they represent the expected costs for a generic connector that we produce.
  It may be that these are costs for the standard market segment. Hence, this would be to figure out how much OE ACC has in the standard segment.
  It also may be that these are expected costs for ACC, reflecting an average of actual historic costs (including both custom and commodity parts)

## Slide 8: Analyzing the Cost Differential: 2. COGS Line item: Depreciation
DC dep = 5.10 – 1.80 = $3.30 US-localized
How much is driven by volume?
Thus: correcting for volume, cost differential becomes DC dep - DC dep, V =
What does this mean?
Notes: How much is driven by volume? Well, the total depreciation (which is the result of past investments and does not change if our actual volumes change) is spread over more units if we were running at higher utilization. The analytics are simple:
explain them for DJC
As an exercise, let’s calculate them for ACC (on slide):
      $5.10/ thousand
      600M
      420M
      420/600= 70%
      $5.10/tho*420M = $2.14M
      85%
      600*85%= 510M
      $2.14/510= $4.20/thou
Check my book formula: Formula c_F = F / R_s = 1.26/800= $1.575. And c_F(Rs/R - 1) = 0.225 = 1.8-1.58. OK!
Correcting for volume effect, cost diff becomes 4.20 – 1.58 = 2.62, which is only $.72 or 22% (.72/3.30) less
What does this mean? Is this good news for ACC?
- No, a small volume effect is bad for ACC because:
even if market picks up, ACC’s utilization would increase, but its cost would only marginally improve, and still be above DJC’s.
If DJC were to enter, it would face similar low volume conditions, but still its cost wouldn’t increase much.
Note:
Because of excess capacity in US market, DJC won’t be able to adopt (at least in the short run) its full-utilization strategy in a new US facility.
Why do we worry about depreciation? Economics tells us that we should price at marginal cost and leave out any sunk and fixed cost. This is true in the short run and corresponds to “dumping.” In the long run, we must cover fixed costs.
Some students may argue that depreciation for DJC in US will increase b/c of new investment. That is true if CapEx in US is much higher than Japan. Otherwise, depreciation horizon will probably be similar so effect would be small.

## Slide 9: Valuing X vs. C Strategy: Breaking up DC into volume, strategic and OE component using trade-off curves
DC
Cost
Differentiation X
ACC
DJC
Hi
Lo
DC
DX
DCv, ACC
DCv,DJC
DCS
DCOE
DC = DCOE + DCS + DCv,ACC - DCv, DJC
Considering depreciation only:
$3.3 = 2.62 + 0.9 - 0.22
DJC’s position if it were to enter our core market
Notes: Recall: the entire objective of the break up calculation is to do volume and strategic, and from that estimate/forecast where the yellow position would fall.
Now: why the minus sign? Well, if you look at the directions of the arrows, it’s clear.
But let’s go back to our depreciation calculation and check it:
The case data was: DC = $5.1-1.8 = 3.3
We calculated that volume effects were (5.1 – 4.2)=.9 for ACC and (1.8 – 1.58) = .22 for DJC
We also found that, correcting for this volume, we got that (DCS +DCOE) = 4.2-1.58 = 2.62.
Now, check the sum: $3.3 = 2.62 + 0.9 - 0.22 INDEED!

## Slide 10: Fixed Asset Utilization

## Slide 11: Asset Utilization Profile: Waste and Value Added Time
Worker
Available time
Waste
Idle time
Meaningless transport
Stockpiling inventory
Fixing defects
Work
Non value add time
Receiving
Unpacking
Setup
Value
add
time
Value add time: Work that directly
increases the product value in the
eyes of the customer or reduces cost
Incidental activity: work that is
necessary to maintain operations
but does not directly increase
customer value or reduce cost
Waste: work that does not add
Customer value and is not necessary
to maintain operations
Notes: Show coffee video to identify waste and incidental activities

## Slide 12: Wasted Capacity Impacts Overall Equipment Effectiveness (OEE) Overall People or Asset Effectiveness (OPE, OAE)
Net
run
time
Idling
and minor
stop-pages
Re-duced
Speed
(quartile plot)
OEE
Defects/
rework
Start-up/
scrap
Avail-
able op’ time
Break- down
Change-overs
Total
planned
up-time
30
55
100
45
Downtime losses
Availability rate
55 %
Speed losses
Performance rate
82 %
X
X
= OEE
30 %
Quality losses
Quality rate
67 %
Improve-
ment potential
> 300%
Notes: Link back to Amazon’s ability to get much higher flow rate from its investment in PP&E.
Show coffee video and point to how waste is reduced and OEE improved in each case.

## Slide 13: The average OEE-values in various process industries range between 40% and 80%
OEE
Poly- ethylen extrusion
Steel: strip metal coating plants
Steel: cold rolling mill
The best practice performance achieved ranges between 85%-95% per industry
80%
75%
70%
65%
55%
48%
45%
40%
0%
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
Food processing
Steel: pickling line
Steel: galvan- izing plants
Plastic films
Casting
Batch chemi- cals
68%
60 %
Steel production incl. continuous casting

## Slide 14: TEEP (Total Effective Equipment Performance over 365 days) = OEE x Loading = 29% v 72%
7
Planned not ope rating (additional)
4
Defects/rework
Non-scheduled (other)
8
Non-scheduled (lower demand/output)
Total planned uptime
Net operating time
Non-scheduled (safety capacity)
Breakdown (process failure)
Available operating time
Startup losses/ scrap
0
Idling and minor stoppages
7
Reduced speed
0
0
0
2
Changeovers
Fully productive time = OEE
20
Year
Plant operating time
Planned not ope- rating (vacation/we)
Planned shutdown (preventive maint.)
15
-28%
8
23
-71%
23
15
6
0
0
0
17
ACC
DJC
In days
Availability
Performance
Quality = OEE
x
x
66% x
100% x
95% = 63%
94% x
100% x
99% = 93%
Loading
46%
78%

## Slide 15: Analyzing the Cost Differential: 2. COGS Line item: Depreciation (cont’d) and Fixed Costs
DOEE can also be broken up
  About 64% of DOEE, net of volume effect, is strategic (assuming no weekend work)
It seems reasonable (best we can do) to assume that DC depreciation , net of volume effect, follows similar split:
DCOE, depreciation ≈ 36% * $2.62 = $0.96
 | # of days |  |  |  |  | 
Per Year (1991) | DJC | ACC | D = | Dvol | + Ds | + DOE
Effective utilization | 264 | 106 | 158 |  |  | 
due to volume: Non-scheduled (lower demand/output than planned) | 38 | 23 |  | (15) |  | 
Effective utilization, adjusted for volume: |  |  | 173 |  |  | 
Process change-over | 7 | 17 |  |  | 7 | 2
Preventive maintenance | 7 | 8 |  |  |  | 1
Process failure | 4 | 31 |  |  |  | 28
Quality losses (re-work, scrap) | 2 | 6 |  |  |  | 3
Planned not operating (vacation/weekends out of 350days) | 20 | 100 |  |  | 80 | 
Planned not operating (additional out of 365days) | 15 | 15 |  |  | - | 
Non-scheduled (safety capacity) | - | 23 |  |  | 23 | 
Non-scheduled (other) | 8 | 37 |  |  |  | 29
 |  |  | 173 |  | 110 | 63
 |  |  | 100% |  | 64% | 36%
Notes: This is also called a utilization profile, very important and worthwhile to discuss in detail per line item (be prepared to discuss two first rows in detail!):
Scheduled availability:
is the total amount of time we plan to have the plant “open and staffed.” Notice that ACC does not work weekends, which amounts to 80 days less (the remaining 2*52-80=24 days is vacation etc.)
It can be argued this is one way of implementing a 22.9% safety capacity relative to DJC. Recall queuing: safety capacity is necessary for allowing high responsiveness.
On the other hand, the strategic choice for responsiveness was 85%, only 15% relative to DJC's 100%.
Thus the remaining is more scheduled idleness than we strategically wanted, hence OE.
Non-scheduled utilization loss: unclear what this means. Could argue that this is idle time during operating hours (safety capacity) or the result of insufficient demand (slow economy). Indeed, DJC runs 700/800 = 87.5% or 12.5% lower utilization that strategically aimed at; ACC is 420/600 = 70% or 15% lower than aimed the 85% aimed at. These numbers are close to the table’s, but not identical. So, one could argue that it is a combination of volume and OE. Actual volume deviations are 12.5% (DJC) and 15% (ACC), or -2.5% net.
Working backward, we have:
Scheduled operating days 330 250
Strategically targeted utilization 100% 85%
Loss during scheduled operating (absolute days) 0 37.5 days
As percentage of total available time of 350 0% 10.7% -10.7% = strategic idleness
The remaining items are fairly straightforward:
Process failure = breakdowns and downtime to repair. Due to various reasons: running at too high speed, not running proven technologies, process not in control, etc. Smart OM takes care of this = OE
Preventive maintenance = down for scheduled maintenance. More of this would reduce failures. Again, smart OM does this = OE.
Process changeovers = variety related = S. (although even this can be improved using setup time reduction-SMED)
Quality loss = good OM puts quality at source and SPC = OE
Note: this measures productivity!
*Notice that 70% utilization does not match the 30.2% asset utlization number. Reason: different measures (units vs. time +
Rated capacity vs. theoretical capacity).

## Slide 16: Analyzing the Cost Differential: 3. Labor
□ COGS Line item: total labor DCLabor = 10.30 – 3.77*1.1 = $6.15 US localized
ACC is much less efficient than DJC: higher proportion indirect labor (46% vs. 32%) + workers are less productive (1.06 vs. 7.45). With same productivity, ACC would need only 396*1.06/7.45 = 56 workers!
Volume adjustment: none on DL, but on IL: can only compute for DJC to $.75*1.1*700/800=$0.72
  DCLabor + DCLabor,vol,DJC = $6.15 + ($.75 * 1.1 - $.72) = $6.26
Rough estimate OE: One way to determine how much ACC’s labor costs /thousand should decrease if the plant were at capacity (600 million units). Assume that ACC can achieve this without increasing its total labor bill (no additional operating hours or workers are needed).
  Total labor bill is $10.30/1000*420M= $4.3 million (direct and indirect)
  $4.3/420 million units = $10.30/ thousand
  $4.3/600 million units = $7.17/ thousand
  Difference = $3.13/thousand
This increase in labor productivity is best possible. Therefore at least the balance of the cost difference ($6.26 - 3.13 = $3.13) is due to inefficiency, and at worst all of it.
Notes: Focus on the last line: DCOE ≈ $4.7 to $7.8 > 0 out of DC = 13.54 is only 36%. So?
This shows that there is a considerable strategic trade-off between low-cost (DJC) and innovation/responsiveness (flexibility of ACC): more than 60% of the overal cost advantage is from trading off less flexibility for lower cost, which is good news for ACC! In other words: I am siding with Andy Li!
well, our estimate is that DJC would still have a $4 to 7 cost-advantage if it used its processes to target our custom segment and if it can reach its target full capacity (which is unlikely). Not good! ACC’s position is at risk!
But that assumes ACC does nothing. Now use this analysis to design a competitive response!
Remarks on Labor Cost Analysis:
Labor is without question the most “debatable” line item and unfortunately has the biggest impact on DCOE impact That can be interpreted in two ways:
  a weakness of the analytics, or
  it demonstrates that the impact of labor exceeds that of material efficiency and capital depreciation. The debate then centers on the question whether DJC could get the same labor efficiencies in the US.
Another approach for labor is to use exhibit 5 and calculate total number of employees per category.
- then calculate volume effect by assuming IL is fixed. Clearly, the volume impact on ACC will be much larger than on DJC, but this would mean that our labor contracts are not long term and we fire and hire at will to follow the economy. If we don’t, then volume effect on labor is zero and it becomes a mix between strategic retention and OE.
- to find strategic component: control and tech development are perhaps strategically needed for variety and innovation, the rest is efficiency.

## Slide 17: Analyzing the Cost Differential: 4. Electricity & Other
□ COGS Line item: electricity and other
Debatable; probably similar to OH, so could be assigned similar to depreciation and fixed cost:
DCOE, other ≈ 36% * (-$0.32 + $1.86) = $0.56
Notes: Focus on the last line: DCOE ≈ $4.7 to $7.8 > 0 out of DC = 13.54 is only 36%. So?
This shows that there is a considerable strategic trade-off between low-cost (DJC) and innovation/responsiveness (flexibility of ACC): more than 60% of the overal cost advantage is from trading off less flexibility for lower cost, which is good news for ACC! In other words: I am siding with Andy Li!
well, our estimate is that DJC would still have a $4 to 7 cost-advantage if it used its processes to target our custom segment and if it can reach its target full capacity (which is unlikely). Not good! ACC’s position is at risk!
But that assumes ACC does nothing. Now use this analysis to design a competitive response!
Remarks on Labor Cost Analysis:
Labor is without question the most “debatable” line item and unfortunately has the biggest impact on DCOE impact That can be interpreted in two ways:
  a weakness of the analytics, or
  it demonstrates that the impact of labor exceeds that of material efficiency and capital depreciation. The debate then centers on the question whether DJC could get the same labor efficiencies in the US.
Another approach for labor is to use exhibit 5 and calculate total number of employees per category.
- then calculate volume effect by assuming IL is fixed. Clearly, the volume impact on ACC will be much larger than on DJC, but this would mean that our labor contracts are not long term and we fire and hire at will to follow the economy. If we don’t, then volume effect on labor is zero and it becomes a mix between strategic retention and OE.
- to find strategic component: control and tech development are perhaps strategically needed for variety and innovation, the rest is efficiency.

## Slide 18: Competitive Cost Analysis
 | DJC/Kawasaki | DJC @ US | DJC @ US, volume | DCS + OE | DCS | DCOE | ACC @ volume | ACC
RM (product + packaging) | $ 14.89 | $ 8.93 | $ 8.93 | $ 2.56 | $ 2.45 | $ 0.11 | $ 11.49 | $ 11.49
DL | $ 3.02 | $ 3.32 | $ 3.32 |  |  |  |  | 
IL | $ 0.75 | $ 0.83 | $ 0.72 |  |  |  |  | 
Total Labor | $ 3.77 | $ 4.15 | $ 4.04 | $ 6.26 | $ 3.13 | $ 3.13 |  | $ 10.30
Electricity | $ 1.40 | $ 1.12 | $ 1.12 | $ (0.32) | $ (0.20) | $ (0.12) | $ 0.80 | $ 0.80
Depreciation | $ 1.80 | $ 1.80 | $ 1.58 | $ 2.63 | $ 1.68 | $ 0.95 | $ 4.20 | $ 5.10
Other | $ 4.24 | $ 4.24 | $ 4.24 | $ 1.86 | $ 1.19 | $ 0.67 | $ 6.10 | $ 6.10
Total | $ 26.10 | $ 20.24 | $ 19.91 | $ 12.98 | $ 8.25 | $ 4.73 | $ 22.59 | $ 33.79
 |  |  |  | if all Labor is OE | $ 5.12 | $ 7.86 |  | 
(Dollars per thousand units, 1991) |  |  |  |  |  |  |  | 

## Slide 19
Cost comparison DJC versus ACC
Dollar per thousand units, 1991
Origin of cost differential
Drivers
Changing sourcing geographies
DJC costs impacted
Cost indexes
Under-utilization of DJC fixed assets versus plan
DJC target utilization
DJC current utilization*
Fixed assets costs**
* Excluding effects from process changeover (resulting from strategic decisions) and sub-optimal operations
** Fixed assets costs include depreciation and indirect labor cost. ACC indirect labor estimated based on indirect/direct cost premium observed at DJC
Lower utilization, higher setup and inventory costs from increasing SKUs
Raw materials for packaging
Number of SKUs
Holding costs
Setup costs
Process changeover time
Fixed assets costs**
DJC
as is
DJC
in US,
Operating at planned capacity
DJC
sourcing in US
DJC
in US, at planned capacity, delivering ACC value proposition
ACC
operating at planned capacity
ACC
as is
DJC raw material relative savings
ACC relative capacity under-utilization linked to sub-optimal processes
Other unexplained ACC operational deficiencies
Fixed assets capacity loss resulting from sub-optimal processes
Fixed assets costs**
Under-utilization of ACC fixed assets versus plan
ACC target utilization
ACC current utilization*
Fixed assets costs**
D C location DJC
D C (capacity) plan, DJC
D C (capacity) plan, ACC
D C strat,
D C OE
5.85
0.33
4.73
.9
5.12
26.10
20.24
19.91
28.16
32.89
33.79
-
4.00
8.00
12.00
16.00
20.00
24.00
28.00
32.00
36.00
To 8.25
To 7.86
To 25.03
.84
Notes: This is another representation and perhaps easier way to convey our analysis.

## Slide 20: Learning Points: Case: American Connector Company
Assessing competitive operations strategies:
  ACC and DJC have chosen different competitive strategies, resources, and processes
    DJC offers a standard product portfolio (sells a “manufacturing capability”) and is formidable learner
    ACC offers design & mfg customization (sell “customer solutions”) but is not-aligned for 85% of business
  Tools: framework elements + alignment (audit, product-process matrix) + 4 stages
Valuing an operations’ differentiation strategy must correct for differences in
  Location
  Volume and other deviations from planned operating conditions
  Strategic positioning
  This break-down quantifies the trade-offs between competing on cost vs. innovation/flexibility
  The remaining cost differential is attributable to operational efficiency
Designing strategic defense
  On the operations side: Definitely implement operational improvement to eliminate DCOE and safeguard own custom segment
    The magnitude of the different line items dictate the priority in implementation
    Consider “standard segment”: is current process best fit, implement separate tailored process, or exit it?
  On the value side: how can we improve DValue? What is outlook for both segments? Can we rationalize SKU proliferation w/o hampering DValue?
  On the competitive side: Thwart DJC entry: prevent them from gathering scale …
Insights: Bench marking must correct for inherent differences between apples and oranges. Sometimes companies that look like competitors may not be competitors
  Critical to sort out differences due to strategy and those due to pure inefficiency. Without controlling for strategy differences, the situation may look worse than it actually is.
  Use benchmarking to target those capabilities that need improvement to better carry out strategy

## Slide 21
Notes: Update (Aug 29, 2011):
Xoom now sells for $499 for WiFi (can’t seem to find the 3G model); same as iPad2, at Best Buy.
HP wanted to discontinue its tablet and discounted it to $99 yet it costs $306: http://online.wsj.com/article/SB10001424053111903352704576540982671537062.html?mod=WSJ_hp_LEFTTopStories
http://operationsroom.wordpress.com/2011/03/08/whos-xoom-ing-who-why-dont-new-tablets-match-apples-price/
Marty relates to the unusual: Apple seems to be restricting the supply of iPads to retailers so Apple continues to call the shots and gets the retail price it wants while getting broader distribution.
@Tallys: I don’t think Apple considers the iPad (or for that matter the iPhone) to be a low-margin opportunity. On the contrary, I believe that the iPad might deliver approx 40% gross margins (you have to add $125 for royalty, assembly costs and some room for field failures and returns to the $278 number above).
The iTunes store (apps and multimedia content) is a nice addition to Apple’s revenue stream – it generated ~$1B in sales in Q1 2011, but it cannot be considered to be a larger profit engine (in absolute numbers) for Apple relative to the iPad.
@Prof. Lariviere: The only reason I can think of why the XOOM is priced so highly relative to the iPad (or iPad2) is that Motorola expects the XOOM prices to drop once the iPad2 is announced/launched. I would be shocked if they are able to sell volumes at this price point.
With a starting price of 799, the XOOM would be still be able to deliver approx a 50% margin (with the same assumptions around royalty and assembly costs), but if they drop the prices to $500 (iPad2 price) their margins drop to ~25% – which is Motorola Mobility’s overall gross margin. I would expect Motorola to move volumes when they hit a ~$600 retail price point on the XOOM coupled with subsidies from operators like Verizon.
Disclaimer: I used to work in the Product Management organization at Motorola Mobility.

## Slide 22: What’s behind the trade-off curves?
Cost – Variety: Setup/changeover costs
Cost – Time: Excess Capacity
Cost – Quality: Inspection/Rework/Warranty

## Slide 23: Cost-Variety Scaling: Changeovers
Changeovers: ACC: 16.8 days or 4.8%; DJC: 7 days or 2.0%. Is all of this difference due to strategy?
If ACC could adopt DJC’s smart changeover capabilities, how much changeover time would it save (= OE)? What would DJCs changeover time be if it were to execute ACC’s position (= strat)?
  Increase #SKUs N from 640 to 4500 while reducing total annual throughput rate R from 700m to 420m
  Recall EOQ:
    throughput per SKU = R/N
    Q = sqrt(2*(R/N)*S/H)
    # changeovers per SKU per year (R/N)/Q = sqrt(RH/2SN)
    Thus, total # changeovers per year = sqrt(RHN/2S) is proportional to sqrt(RN)
  Thus, if DJC were to execute ACCs position--match # SKUs (increases by factor 7.03) and volume (decreases by factor 0.60)--then DJCs change-overs would increase by factor sqrt(7.03 x 0.6) = 2.05
  So, DJC’s total changeover time goes from (days) 7 to 14.4 = due to strategy
    ACC would save 16.8 – 14.4 = 2.4 days = due to OE

## Slide 24: Summary Guidelines
Know your operations cost structure & Get to know your competitors!
  Estimate your trade-off curve and theirs
  Models help; sometimes must use rough estimates
Don’t use cost numbers at face value. Rather, adjust for strategic positioning and volume (utilization) differences to arrive at the cost advantage due to operational efficiency, which is the meaningful “net cost advantage” number.
Base your OE improvements on:
  your competitive knowledge
  and use the concept of focus & good operations management
Be mindful of productivity measurements because they do not adjust for strategy differences and bring with them a focus on cost only.

## Slide 25: Estimating the Value Differential and Assessment of the Threat
We expect a differentiation strategy to be more costly (DC > 0), but also to command higher prices (reflecting the increased customer value)
How large is the differentiation advantage for ACC?
  Value(D X) = D WTP ≈ D price
  Recall that gross margin percentage gmp = (p - c)/p so that
  Dp = DCOGS/(1-gmp) = $33.79/(1-.43) – 26.10/(1-.50) = $59.28 - $52.20 = $7.08
  Careful: this averages over both of ACC’s segments + DJC may change price in US.
Evaluation of differentiation strategy: is it worth it?
  Key condition: Value(DX) > DC? $7.08 v. $7.69 (US adjusted: $19.78 v. $13.54)
Assessment of the threat:
  If no: then ACC’s strategy is in serious jeopardy: DJC could conceivably use its current operating system to produce its current products and offer those to our customers at a price discount that exceeds the value that customers currently place on ACCs differentiated products
  If yes: the ACC’s differentiation strategy is viable. However, what would happen if DJC enters and:
    DJC use its current operating system to produce differentiated products and services (ACC’s niche): would DJC still have a cost advantage?
    DJC targets only the low-cost standard segment: what can ACC do to protect itself?
Notes: Recall that our goal is to come up with a recommendation to Denise using the following plan:
Assess the situation by contrasting ACC and DJC’s OS. This is an application of class 1. Done
Analyze the sources of the cost differential. Let’s now analyze the cost differential, focusing on ACC’s process for its custom segment b/c that’s the question we’re interested in.
Assess the threat and recommend a plan of action.
How large is the differentiation advantage for ACC?
  A proxy for Value(DX) is DPrice. How find price, given that we have COGS?
  Recall: GrossMarginPercentage gmp = (p-c)/p → p = COGS/(1 – gmp)
  [don’t confuse with MarkUpPercentage mup = (p-c)/c → p = COGS x (1 + mup)
  but:
  this is only a proxy; DJC may change its margin and price when coming to US. Thus, use this only at current (un-localized) prices.
  This margin number is either an average of both segments, or 0% for standard (in which case custom would be 43%/0.15 = 6 x 43%!)
Key condition: The D inequality: Value(DX) >? DC
    If yes: the differentiation strategy is more profitable (per unit). But there are still two competitive forecast scenarios to consider:
    STRESS THE TWO QUESTIONS, THIS IS KEY.
    We will consider as main question: what if DJC were to copy us?
    How do we answer the last two questions? We must correct the cost differential for any change in strategy (and volume), the remainder is OE.
    We shall first try to estimate what cost advantage remains for DJC if it were to compete in our niche (which will increase its costs). Then we will ask ourselves what ACC can do to protect itself in that segment (and also to protect its standard segment).

## Slide 26: Recall the three definitions
DCV is the volume-(or utilization) driven cost differential
  These are the extra costs incurred by operating at less than the strategically-targeted utilization level because of spreading a fixed cost over fewer units
  Why have this?
DCS is the competitive strategy-driven cost differential
  This is the cost difference inherent in the way each company chooses to compete.
  We would expect that a strategy emphasizing product innovation and customer responsiveness is more costly than a pure low cost strategy
DCOE is the operational efficiency-driven cost differential
  This is the remainder of the cost differential after controlling for volume and strategy.
  It measures how one company is just more efficient in their operations and management than another, even if both were to run at their desired utilizations and to provide identical value proposition.
Notes: DCV is cost of “non-strategic” excess capacity, resulting from insufficient market demand. (Less than we targeted.) It really measures loss of scale economies.
To illustrate and make sure we all understand what is meant by DCV consider ACC:
What is ACC’s capacity? 600M units/yr
What utilization does it strive for strategically? 85% = 510 M/yr
But what is its current utilization? 70% = 420 M/yr
The difference between 1 and 2 is due to strategy, between 2 and 3 is due to lower volume sold than we aim for. That is what we call the volume-driven cost differential. We isolate this effect b/c we want to assess the cost of the process if it were to be operated under conditions that we strategically plan for. Ch 2: “DCS is the change in cost due to a change in market positioning only.”
Let us now estimate this cost breakdown for COGS by looking at each line item in detail. (Actually, we’ll focus on RM and FC (depreciation) and my numbers are just one example of how it can be done. Some allocations are judgment calls. Let’s discuss those when we get at them and tell us what you did.) Note that we really should look at Total Landed/Supply Cost = COGS + working capital [which include service and inventory concerns]; we’ll do that in two weeks with Offshoring and Mex-China.
Our game plan: Estimate the fraction of total DC = $13.54 that is due to operational efficiency, because that is the part that matters if DJC were to enter ACCs market and adopt its product strategy (or what ACC can improve)
Approach:
  for each line item in COGS: Break up its contribution to total DC into (1) volume, (2) strategy and (3) OE
    Result: DCOE, line item i
  Then sum all line items to arrive at an estimate of DCOE
    Result: DCOE = S i DCOE, line item i
Based on the magnitude of DCOE :
  assess the threat: Magnitude of the threat follows the magnitude (and sign) of DCOE
    Why? In words, what is DCOE? It is DJC’s cost-advantage if it were to produce differentiated products like ACC with its current processes and resources.
  and design a strategic response

## Slide 27: Summary so far: Understanding your and your competitors’ trade-offs are key to operations strategy
Process Flexibility
BJG
Unit Cost
low
high
low
high
Operational Trade-offs
Custom design
Job shop process
Standard design
Flow shop process
C&D
Aerospace
Trade-off Principle: Operational competencies are governed by trade-offs that result from the specific operational system of assets and processes.
Customization
BJG
C&D
Aerospace
Total Cost of Ownership
low
high
low
high
Customer Trade-offs
Private jet owner
Commuter airline
Notes: Discuss this well:
First focus on two customer groups, explain their preferences and how that translates into their trade-offs between customization and cost. These trade-offs allow firms to occupy different positions and, doing so, segment the market.
However, key to sustainability is that neither firm can easily straddle and also occupy the other position. This requires similarly strong process competency trade-offs (right). Notice that BJG’s job shop process would have higher cost than C&D if it tried to go for standard designs, similarly for c&D if it were to go for high flex.
Key message: A firm cannot straddle without running a cost disadvantage or without changing its process. Hence the key role of process trade-offs.

## Slide 28: Why estimate trade-off curves? Examples
Fast-casual restaurants: Who’s the top tamale?
  Chipotle (McD) v. Baja Fresh (Wendy’s)
  Price for steak burrito: $5.60 $5.95
  2003 US Sales: $321M $312.5M
  Change since 2002: + 42.7% + 25.5%
Ameritrade’s 5-second guarantee: “Qualified S&P 500 Internet trades that take longer than 5 seconds to execute are commission-free.”
  Flat commission fee = $10.99 per Internet trade
  Average execution time = 1 sec
  Ameritrade reported 144,000 trades per day on average in May 04.
  Impact on value?
Notes: Other examples of variety-cost tradeoffs:
Fast-casual Mexican restaurants: Baja Fresh (Wendys), which has a broad menu, vs Chipotle (McDonalds), which has only 17 menu items (basically burritos and tortilla’s)
Timken: in response to low-price competitors focusing on one product and killing them on price, Timken started
  bundling lubrication functions with the traditional friction function of bearings
  Bundling service (installation, maintenance and ongoing engineering services)
  This requires: investments in R&D, flex plants, customer relationship management (educating customers + staying current with their needs) which also fights offshoring
Contract manufacturers: Plexus (PCB supplier to Unisys; boards cost 80 cents to $60,000 with median around $1,000:
  They use a “low-high strategy,” shorthand for low-volume production of a high mixture of things. They focus on lean ops and quick changeovers with only 20% of labor time goes to changeovers, maintenance and meetings) compared to Solectron.
  Use 4 focused PIP’s because the workload over entire mix differs too much to keep good capacity utilization balanced.
ACC-DJC case next class, at least to model the inventory and setup costs

## Slide 29: Analytics: Estimating Trade-off Curves
Express the cost of providing a certain competency bundle (Time, Flex, Qual) using our operations analytics toolbox.
Examples: Wilbur Chocolate
  How sensitive is Wilbur’s cost structure to changes in variety?
  Build up the minimal sustainable cost of producing N chocolates on a single batch process
Notes: Next time: set up an numeric example as homework

## Slide 30: Analytics: Variety-cost trade-off Wilbur Chocolate
1
10
20
30
40
50
60
70
80
90
100
Product Selection N
Unit Cost c (inverted)
$1.12
$1.10
$1.08
$1.06
$1.04
$1.02
$1.00
Batch process
The choice of operational system shapes the trade-off curve
1
20
40
60
80
100
$1.00
$1.02
$1.04
$1.06
$1.08
$1.10
$1.12
Unit Cost c
Product Selection N
Batch process
Job shop
Job shop
Flow shop
Flow shop

## Slide 31: Analytics: service-cost trade-off Ameritrade
Expected unit warranty cost of poor QoS = $10.99 Pr(execution time > 5sec)
  Queuing theory (Appendix C): Pr(T > t) = exp(-t/average flow time)
  Cost-Service trade-off: c = $10.99 exp(-t)
$10.99
$8
$6
$4
$2
$0
Cost Efficiency (inverted c)
10sec
8sec
6sec
4sec
2sec
0sec
Quality of Service (inverted t)
Cost of Service Guarantee c (log-scale)
dollars
$10
$1
$.1
$.01
$.001
0sec
2sec
4sec
6sec
8sec
10sec
Guaranteed Execution Time t
dimes
cents
Ameritrade’s
5 second guarantee
Ameritrade’s
5 second guarantee
Increased variability
Increased variability
Notes: Do explain trade-off between QoS and cost in detail.
Ameritrade: trade is commission free if execution time T exceeds 5sec. Recall that average execution time is 1 sec.
So, what is the cost of this guarantee? Lost commission. Expected(lost commission) = p x Pr(T>5sec). Think of EVA; the cost of the guarantee is a direct reduction of EVA.
We can get a first rough estimate by modeling the computerized trading by a server and simple queue. The analytics are in the book. (or: Recall queuing: T is exponentially distributed with mean 1 sec. Hence Pr(T>t sec) = exp(-t/1) = exp(-t).)
How would you do this for a more complex process? You could simulate the process and then vary the required response time, optimize the process such that the new response time is gotten at lowest cost. When you do this repeatedly for various response times, the associated cost traces the trade-off curve.
What insights do we get from Ameritrade’s trade-off curve?
  They chose the promise nicely under the knee, generating only $3.9M/yr in lost commission.
  What if they doubled the guarantee to 2.5 sec? Cost would be about 12 times higher to $47M/yr! This is a testament of the strong non-linearity in queuing.
  What does an improvement mean here? Shifting the curve outward via:
    Increasing the transaction speed (computers + schedulers)
    Install more CPU capacity, thereby reducing utilization
    Reduce volatility in arrival times.
Similarly for variety, after using an EoQ calculation, you find that cost is sqrt(N).
This curve is applicable to:
ACC-DJC, at least to model the inventory and setup costs
Fast-casual Mexican restaurants: Baja Fresh (Wendys), which has a broad menu, vs Chipotle (McDonalds), which has only 17 menu items (basically burritos and tortilla’s)
Contract manufacturers: Plexus (PCB supplier to Unisys; boards cost 80 cents to $60,000 with median around $1,000. They use a “low-high strategy,” shorthand for low-volume production of a high mixture of things. They focus on lean ops and quick changeovers with only 20% of labor time goes to changeovers, maintenance and meetings) compared to Solectron.

## Slide 32: Improvement and the Efficient Frontier
Improvement creates options to increase differentiation or cost-efficiency
The frontier is the outer envelope of all competency trade-off curves
1
10
20
30
40
50
60
70
80
90
100
Product Selection N
Unit Cost c (inverted)
$1.12
$1.10
$1.08
$1.06
$1.04
$1.02
$1.00
Last year’s position
New options for this year
operational
improvement
1
10
20
30
40
50
60
70
80
90
100
Product Selection N
Unit Cost c (inverted)
$1.12
$1.10
$1.08
$1.06
$1.04
$1.02
$0.96
$1.00
$0.98
Firm 1
Firm 2
Firm 3
Firm 4
Efficient frontier
DcOE
Set of not-attainable
competencies at this time

## Slide 33: How improve operational efficiency? The concept of focus in operations
Focus is a joint property of the process and of how we choose to utilize it.
Focus principle: A focused operation is more likely to have a competitive advantage by being near the frontier.
Unit Cost c
Non-cost competency X
High
Low
A focused process has a consistent operating point on its trade-off curve
Unit Cost c
Non-cost competency X
High
Low
The operating points of an unfocused process are scattered over a large region
on its trade-off curve
Notes: What’s the benefit of focus?
- repetition breeds competence:
  learning and optimization
  less divergence in attention spans
- less trade-offs need to be made so a tailored (optimized) operational system can be put in place
-

## Slide 34: How to focus an operation: Tailored divide and conquer
Cost efficiency
Customization
Quality
Partition products and services into groups with homogeneous competency needs. (The example to the right has 3 groups.) Consider product-line rationalization.
For each group, separate those resources and processes that critically support its value proposition while sharing the others.
Create a charter for each operation to retain focus over time.
One single system shared by three groups
Three separate
systems, each one
focused on one group
Degree of focus of operational system
tailored
degree of
focus
Competency Space
Notes: An essential question in operations strategy and business model choice is to what extent assets and processes can be shared?
What are benefits and costs of sharing?
Examples:
FedEx-UPS mini-case 2
Supply chain distributors:
  WalMart Remix splits its supply chain network into entire warehouses focused on slow movers v. fast movers.
  Kroger uses three tiers of warehouses
  Contrast with Target’s PIPs: “dedicated express lane in its warehouses for hot sellers such as Tide detergent, Crest toothpaste and Bounty paper towels.”
Recall that Plexus also uses 4 focused PIPs.

## Slide 35: Mini-Case 2 | FedEx v. UPS
“…the optimal way to serve very distinct market segments, such as express and ground, is to operate highly efficient, independent networks with different facilities, different cut-off times and different delivery commitments.” FedEx (2000)
“Our express air services are integrated with our vast ground delivery system: one system handling all products. This integrated air and ground network enhances pickup and delivery density and provides us with the flexibility to transport packages using the most efficient mode or combination of modes.” UPS (2006)
Notes: To give you a preview of what OS is about, consider these two quotations. They show a deliberate, and different, choice in operations strategy!
  It is strategic in the sense that this really defines the entire business model: there is talk about market segments (express vs. regular service) and processing network structure, so that it is OS.
  Let me offer you a picture to think about this (next slide):
    market demand segments: express vs. regular
    matched capacity type (“transportation mode”): air vs. ground
    How do you relate the quotations to this picture? [it’s FedEx OS] How represent UPS’s? [substitution arrows]
    Clearly, integration allows: long-haul regular via air or short-haul express via ground [NY visa from Newark but through Memphis!]
The quotations ask whether we should have dedicated or separate networks for each market segment, or whether we should integrate/share processing networks. How would you think about this OS question? In other words, when is network integration advisable; what are the drivers and conditions of value?
Understanding this or similar choices, and thus what drives value, is what this course is all about.
Value of integration = joint local routes + long-haul regular can be air shipped + short-haul express via ground
  This would allow reduction of ground capacity, even slight increase of air, or improve QoS
Key drivers for integration to have value:
  Local joint routes: savings small if separate segments have high demand, high customer densities or if they live in separate areas; can be large otherwise. Draw route example.
  Long-haul routes: savings small if there is little opportunity to have ground go by air. Depends on: fraction of regular/express, correlation between the two, and excess air capacity, which is driven by demand variability (seasonality + uncertainty in express) and supply variability (how predictable are our flights: weather, #of hubs, control, etc.)
    Clearly, savings increases in regular/express (but with asymptote: at a certain level all excess capacity is used up) and in variability. Draw picture.
    More on cost of QoS (NYT 2005 in folder for Ata_VanMieghem paper)
So what is our insight and recommendation on network integration? When value > cost of integration, i.e., …
  Driver against integration: future spin/sell off. This is what makes it hard for WalMart to sell off Sam’s Club b/c they use the same distribution network and even parking areas!
This example illustrates the core goal of this course: understand key elements of OS and their drivers s.t. you can analyze and value different OSs and implement the one that is best for your organization. In other words, find the best “means” for your “end” or objectives.
  Also an illustration of how our framework which takes an integrative look at strategy with highlight on ops. Topic for today: a good OS installs a tailored operational system.
  Also illustrates substitution flexibility and one way of what we will call operational hedging. (Chapters 5 & 9).
  While this focuses on capacity supply management, we will extend and also look at demand management to maximize revenues from our capacity. (Chapter 8)
Ground
facility
Air
facility

## Slide 36
5.85
0.33
4.40
1.74
7.74
26.10
20.24
19.91
27.65
32.05
33.79
-
4.00
8.00
12.00
16.00
20.00
24.00
28.00
32.00
36.00
± 1.12
± 1.12
± 1.12
± 1.12

## Slide 37: Tradeoffs and Operations Strategy
Operating Metric
(e.g., order fill rate)
Operating Cost
(e.g., inventory)
Operations Management:
Make sure you’re on the efficient frontier given your existing structure and infrastructure
Operations Strategy:
Create a more favorable frontier by redesigning the structure and/or infrastructure
Notes: Optiant Imation Story
Phase 1: Optimize inventory levels and locations given current operations structure: getting to the efficient frontier for service level and inventory investment.
Phase 2: Redesign the operations structure to move the efficient frontier.
Operations management is about achieving the performance frontier and operations strategy is about moving the frontier.

## Slide 38
Operations Strategy (3)
Competencies, Trade-offs & Competition
Why competitive cost understanding is important
  Internal view + External view
How to analyze a competitive threat
  Cost Advantage Analytics using trade-off curves
Design strategies to improve competitive advantage through operations
    Case: Sugar & Spice
    Case: American Connector Corp. (ACC)
Notes: 2011 Plan for 1.5hr ACC class: (actuals in parens)
3:30pm: facts: few leaders leverage competitive info as much as they could. Today we want to see how what we’ve seen so far in the course, all comes together using the ACC case.
3:35pm: do 45min on BB showing the value of differentiation, localization, and volume adjustments.
4:20pm (actual was 4:40 here): move to slides
4:50pm: summary using the trade-off curves
2009 Plan for 3 hr class:
- do ACC case before break
- after break: why comp analysis is important, brief lecture on trade-off curves and productivity, mini-case 2 as second example.
- if time permits: introduce capacity strategy and Harley case.
Actuals: ACC analysis took 1:45hr, break, I summarized after the break. Then did mini-case 2 in last 10min of class.
2007 Plan for 1.5hr class: (actuals in parens)
1:30pm: projects + review last class + related thoughts
1:40pm: competitive cost understanding
1:45pm (past 2pm): tradeoffs: examples + analytic models—Next time I’ll set up a numerical example for homework for them to figure out the selection-cost tradeoff.
2:25pm (2:45pm until 3pm): role of trade-offs w/frontier & competitive cost analysis
2:45pm (did not get to): role of focus and productivity
Plan for 3hr night class: (actuals for Wed/Th 2005 classes;Wed/Th 2004)
6:30pm: opening and admin
6:35 (6:35/6:35; 6:35/ 6.34): ACC evaluation, analysis, and action (students)
7:15 (7:30/7:30; 7:29/7.19): my take on ACC analysis (my slides)
7:55 (8:10/8:10; 8:16/8.14): ACC summary
8:00 (8:20/8:17; 8:25/8:14 before action plan): break
8:15 (8:35/8:32; 8:39/8:45): Theory and Analytics
9:05 (NA/NA; 9:13 /9:17): Productivity
9:20 (9:20/9:20; 9:27/9:29): next class
9:30 (9:30 /): end

## Slide 39: Manufacturing leaders claim they focus on being cost competitive more than they focus on any other priority…
91%
84%
67%
63%
42%
40%
16%
5%
12%
26%
19%
44%
28%
49%
4%
2%
2%
14%
14%
30%
30%
2%
5%
4%
2%
5%
0%
10%
20%
30%
40%
50%
60%
70%
80%
90%
100%
How to be cost competitive
How to deal proactively with
safety/quality issues
What type of measurement system
to use to track performance
How to motivate the work force
How to implement TPS, Six
Sigma, TQM, etc.
The geographical network of plants
Vertical integration (in-house
manufacture vs. outsource)
Tasks for Manufacturing Leaders
Percentage of Survey Respondents stating High, Medium, Low Priority or N/A
Note: 40 percent of the interviewees proposed additional tasks
Source: Booz Allen Hamilton/IPSOS-MORI survey of manufacturing leaders
Notes: “How many of you would say that your most recent organization had a good understanding and data on competitor’s cost structure?”
[in 2007: both sections had about 30-35% of the students raise their hands—in line with the data on later slides. This led to a good discussion of how they get that data.]

## Slide 40: …but they actually know little about competitors’ costs…
33%
56%
8%
3%
0%
60%
Percentage Who Responded “Yes” to each statement
You understand very well your own
detailed cost structure and those of
your competitors
You know your own manufacturing
cost structure well, but are unclear
about those of key competitors
You understand some aspects of your
manufacturing cost structure, and little
of those of your key competitors
You aren’t concerned by your cost
structure or those of competitors;
others follow that within your company
Source: Booz Allen Hamilton/IPSOS-MORI survey of manufacturing leaders

## Slide 41: …and when making decisions, they typically don’t leverage competitive information as much as they could.
70%
67%
51%
33%
0%
80%
Company financial targets translated
into expected contributions
Detailed studies of the operations
Comparisons of plants internally
Comparisons with competitors
or players in other industries
Percentage Who Responded “Yes” to each statement
Source: Booz Allen Hamilton/IPSOS-MORI survey of manufacturing leaders