## Slide 1: What’s behind the trade-off curves?
Cost – Variety: Setup/changeover costs
Cost – Time: Excess Capacity
Cost – Quality: Inspection/Rework/Warranty

## Slide 2: Cost-Variety Scaling: Changeovers
Changeovers: ACC: 16.8 days or 4.8%; DJC: 7 days or 2.0%. Is all of this difference due to strategy?
If ACC could adopt DJC’s smart changeover capabilities, how much changeover time would it save (= OE)? What would DJCs changeover time be if it were to execute ACC’s position (= strat)?
  Increase #SKUs N from 640 to 4500 while reducing total annual throughput rate R from 700m to 420m
  Recall EOQ:
    throughput per SKU = R/N
    Q = sqrt(2*(R/N)*S/H)
    # changeovers per SKU per year (R/N)/Q = sqrt(RH/2SN)
    Thus, total # changeovers per year = sqrt(RHN/2S) is proportional to sqrt(RN)
  Thus, if DJC were to execute ACCs position--match # SKUs (increases by factor 7.03) and volume (decreases by factor 0.60)--then DJCs change-overs would increase by factor sqrt(7.03 x 0.6) = 2.05
  So, DJC’s total changeover time goes from (days) 7 to 14.4 = due to strategy
    ACC would save 16.8 – 14.4 = 2.4 days = due to OE

## Slide 3: Summary Guidelines
Know your operations cost structure & Get to know your competitors!
  Estimate your trade-off curve and theirs
  Models help; sometimes must use rough estimates
Don’t use cost numbers at face value. Rather, adjust for strategic positioning and volume (utilization) differences to arrive at the cost advantage due to operational efficiency, which is the meaningful “net cost advantage” number.
Base your OE improvements on:
  your competitive knowledge
  and use the concept of focus & good operations management
Be mindful of productivity measurements because they do not adjust for strategy differences and bring with them a focus on cost only.

## Slide 4
Operations Strategy (4)
Strategic Capacity Sizing and Investment
The concept of a capacity strategy
Capacity strategy models: key elements to capture
Incorporating risk
Notes: 2012: The key points I want them to take away are:
- What is a cap strategy?
Our main focus is on how to build models to guide capacity strategy; key attention goes towards incorporating risk:
  in models
  in the process of risk mgt and hedging

## Slide 5: Operations strategy & Principle of value maximization
Assets
Sizing: What should overall capacity be?
Type: What kind of assets are best?
Timing: When expand or contract capacity?
Location: Where locate assets?
V
A
P
C
Value
Capabilities
Processes
Notes: Example: Sharp: C = low cost and reasonably timely, A = new plant, P = new 8 x 40” panels, moving 17 outside suppliers and service providers inside to work as “one virtual company”, hyper JIT. (how set up terms? Suppliers built and pay own facility, rent land from Sharp, but can sell to outside). Should glass supplier Corning also move?
We have viewed ops as resources applied to processes. Obviously the choice of resources and processes gives ops certain competencies: they affect what the organization can and cannot do. We will summarize the competencies by 4 dimensions & prioritize them: order winners vs. qualifiers.
  What are our distinctive capabilities or competences?
    “The combinations of resources and processes that underpin sustainable competitive advantage for a specific firm competing in a specific market.”
    “Abilities that customers value but that competitors cannot replicate.”
  Are competencies fully determined by resources and processes? Values = standards by which employees set priorities. When they are set automatically (by process) they constitute the culture, which allows decentralized aligned decision making.
Value = 3 P’s = profit, people, planet
Consider profit: We thus have a clear metric for evaluation and improvement of OS: NPV
  We always want to make sure our recommendations are financially sound. After all, why are we in business?
  Performance metrics: many, including survival, growth, profits, shareholder value and others. Our metric will be profit flows, that is the complete current and future stream of profits. From this, most other financial metrics can be deduced.
The main advantages for NPV of cash flows are:
  In-line with financial theory
  Cash flows are harder to manipulate than a single measure;
  they recognize the longer term and temporal character of many decisions, yours as well as your competitors’
  they allow us to incorporate risk attitudes and uncertainty.
But be cognizant that not everything is properly expressed in money! Always consider people + planet!
Maximizing NPV gives us a quantitative tool, but it only works well for determining correct parameter choice + choice between alternatives.
  The next slide details the typical components of the resource and process view that you can work on; abstractly, these are the “parameters” you could optimize over
  To come up with the alternatives, we use qualitative judgment and experience.
    A qualitative tool to help us: alignment and 3 questions framework.

## Slide 6: Some recent capacity announcements
New vaccine factory in Brazil
Cost = $300-$500M
New fabrication plant in Germany and expanding capacity in USA
Cost = $3 billion
Modernize transmission plant in Indiana
Cost = $1.1 billion

## Slide 7: Capacity Planning Hierarchy
Tactical
Capacity Planning
Strategic
Capacity Planning
Executional
Capacity Planning
Time Horizon
Planning Buckets
Decisions
0-30 days
1-18 months
1-5+ years
Hours or days
Weeks or months
Quarters or years
Schedule for existing resources
Optimal allocation of existing capacity
Capacity levels of easy-to-flex resources
Capacity expansion (contraction) of hard-to-flex resources
Capacity technology
Capacity location
Our Focus
Notes: Explain “easy-to-flex”
Strategic horizon can exceed 10 years in some industries, e.g., 15 years in pharma.
Other names used in practice:
Strategic: Resource requirements planning, the counterpart of demand management, both of which feed into long range production planning.
Tactical: operates at two levels:
  the long range production plan feeds into the master production schedule (MPS) of end items, which is capacity agnostic. Therefore, validating the feasibility of the MPS using “rough-cut capacity planning” is very important.
  The MPS feeds into the MRP covering both released orders and planned orders of input items (which again is capacity agnostic). Use these releases into a detailed planning of CRP.
Execution.

## Slide 8: Capacity & Investment
Capacity = maximal sustainable throughput
  Network capacity is limited by bottleneck resource(s)
  Depends on product mix
Distinguish
  Capacity Investment cost (CapEx)
  Operating cost (OpEx)
Bottleneck Capacity
OEE
Maximal sustainable throughput
Units/hour
Annual Capacity
Units/year
Loading
TEEP

## Slide 9: Factors that Influence Capacity Strategy
Scale Economies (Capacity & Production)
Technology Roadmaps
Competitor Actions
Customer Stickiness
Supply Base
Access to Capital
Time Value of Money
Uncertainty
Demand Growth Curve
Learning Curves
Capacity Strategy
Notes: JVM: during our course, we will focus on the 5 top ones.
Today, most attention to uncertainty. Why? McK states:
‘Redesigning the footprint can be the biggest and most important transformation a manufacturer can undertake. Yet too many managers choose the footprint by using only a single set of future cost and demand assumptions.”
“In our experience, the missing ingredient in many manufacturing strategy decisions is a careful consideration of the value of flexibility.”
Slide is blank for students.
Ask students for relevant factors.
Demand growth curve
  2010 WSJ LED article (not assigned). “The market for light-emitting diodes is expected to boom in coming years … The DOE (dept. of energy) predicts that LEDs will make up 70% of the lighting market by 2020, up from less than 1% now.”
Scale economies.
  Production -> Chinese manufacturers, heavily subsidized by their own government and relying on vast economies of scale, have helped send the price of conventional solar panels plunging and grabbed market share far more quickly than anyone anticipated. (Assigned Solyndra article)
  Capacity ->?
Learning curves
  2007 WSJ article (not assigned) “The semiconductor industry and its suppliers are mounting a long-term campaign to wring productivity improvements from existing factories, without a costly shift to larger wafers and new tools to process them.”
Technology roadmaps:
  “For TI, the factory further marks its shift from selling technology that connects cellphones and toward the larger, more profitable and fractured market for analog chips, which are used to manage power, convert data into digital signals and complete other tasks in nearly every electronic device.” (Assigned TI article)
  “AQT has modified off-the-shelf machines used to make computer hard drives to create CIGS cells using a proprietary process. The Sunnyvale company, which has raised $15 million from investors, further cut its capital costs by manufacturing only solar cells, which it sells to other companies to package into solar panels.” (Assigned Solyndra article)
Customer stickiness:
  “As part of its corporate sustainability policy, Wal-Mart Stores last month acted to bolster American CIGS companies by signing a deal with a Silicon Valley solar installer, SolarCity, to put 15 megawatts of photovoltaic panels on its big-box stores and requiring that a significant percentage of them come from thin-film companies like MiaSole. Even so, SolarCity's chief executive, Lyndon Rive, acknowledged that his company would also be installing a large number of conventional solar panels for the retail giant -- nearly all of them made in China.” (Assigned Solyndra article)
Competitor actions:
  “But as the companies finally begin mass production -- Solyndra just flipped the switch on a $733 million factory here last month -- they are finding that the economics of the industry have already been transformed, by the Chinese. Chinese manufacturers, heavily subsidized by their own government and relying on vast economies of scale, have helped send the price of conventional solar panels plunging and grabbed market share far more quickly than anyone anticipated. As a result, the California companies, once so confident that they could outmaneuver the competition, are scrambling to retool their strategies and find niches in which they can thrive.” (Assigned Solyndra article)
Supply Base
  Example: See Plambeck paper with solar and wind power discussion. (I’ve printed pages 3-4).
Access to capital:
  “The federal govt provided a $535 million loan guarantee for [Solyndra’s] new solar panel factory know as Fab 2.” “Chinese companies rapidly expanded production …. Supported by tens of billions of dollars in inexpensive credit from the Chinese government as well as other subsidies such as cheap land.” “[VC] investors [are] skittish about backing new capital-intensive start-ups.” (Assigned Solyndra article)
Time value of money:
  Relative to inflation
Uncertainty:
  “The solar market has changed so much it’s almost enough to make you want to cry.” CEO of MiaSole. (Assigned Solyndra article)
We will focus on scale economies, demand growth curve, time value of money. Will come back to uncertainty later. Beware, no one model can incorporate everything and deliver an answer that won’t be adjusted by senior management.

## Slide 10: Tesla’s Capacity Shortage: Measurement and Valuation not obvious
Continuing shortfall in lithium-ion battery cell supply was the biggest obstacle that prevented Tesla from selling more.
CEO Musk: That shortage prompted us to create plans for Gigafactories.
“For us it’s critical to have the first gigafactory ready on time,” said Deepak Ahuja, Tesla’s chief financial officer, during the earnings call. “Every month of delay is far more expensive for us than the incremental cost upfront to kickoff two sites at one time.”
“Tesla makes fast move to build two giant battery factories simultaneously,” Forbes, 5/07/2014

## Slide 11: Incorporating risk: why and how 4 Levels of Residual Uncertainty
1
2
3
Level 2
Alternate Futures
Level 1
A Clear-Enough Future
Level 3
A Range of Futures
?
Level 4
True Ambiguity
Courtney, Kirkland and Viguerie: Strategy Under Uncertainty. HBR Nov-Dec, 1997
after including all the info
you COULD obtain
Notes: Often, capacity investment decisions start with an NPV analysis. As we will show in Harley, then it becomes clear that most of the differences in results stem from differences in how risk was incorporated. You can decompose profit and see how it depends on demand and capacity in various places. And, given that demand is random, the interaction is tricky and you need to be clear on how to model it.
So then we can go into discussing how to incorporate risk.
In practice, many people tend to move to one of two extremes: 1 (you know exactly what’s going to happen) or 4 (you have no idea).
In reality, you typically find yourself, with a little bit of effort, in 2 (finite # of scenarios) or 3 (continuous distribution).
For many things, prediction markets work very well; this means that for many things, you can make predictions and true ambiguity is rare in the settings that we consider.

## Slide 12: Bain & Company identifies three types of commonly used capacity planning forecasting methods
CPG Co
“We only use one number today, although we may move to a range forecast”
Fmr Market Researcher, CPG Co.
High utilization strategy
Inexpensive, smooth CAPEX
Smooth, low variance, controllable demand
One number
Industry examples
When used
Typical migration path as (1) planning processes mature, (2) organization learns to better model and plan for uncertainty, and (3) cost of “being wrong” increases in capacity decisions
Auto Co
Biotech/Pharma Co
“Our process looks at indications for each product, and probability of success… leading to a Monte Carlo simulation to create a range forecast… We then use base demand & upside demand points on this curve to plan capacity”
Forecast planner, Biotech
“We use a full demand distribution… and use flexible plants to meet that demand”
Dir, Supply Chain Strategy, Auto Mfr
“Never miss a sale” strategy
Expensive, lumpy CAPEX
Lumpy, high variance, hard to control demand
Full distribution/range
Forecasted demand probability
Tech Mfg Co
“We forecast a range… expected demand, and an optimistic and pessimistic scenario”
Fmr Tech Mfg Executive
“ON Semi. creates low, medium, and high demand scenarios along with capacity plans for each.”
i2 Technologies Case Study
Mixed utilization vs. sale strategy
Moderate CAPEX variance
Moderate control of demand
Need / desire for something “simpler” than full distribution
Multiple scenarios
Forecasted demand probability
Forecasted demand probability
Reproduced by permission from Bain & Company; it is not to be relied on by any 3rd party without Bain's prior written consent.
Notes: It can be argued that these approaches reflect the different means served:
One number = this really reflects more the sales plan, the objectives
Only the other two are true “demand forecasts”.
Leading on question: so if you forecast, what is it that you are trying to forecast?

## Slide 13: Forecasts
Principle: Forecast should include all predictions on the evolution of relevant factors:
  Demand
  Supply
  Technology:
    Cost of capacity
    Learning and continuous improvement increase capacity (yield)
    New technologies
  Strategic Uncertainty: Competition and environment
Principle: Forecasts should include uncertainty by time bucket.
Challenges in practice:
Many companies use only point forecasts
Forecasts require cross-functional input and agreement
Most important: forecasts can serve two means:
  Goal setting, often connected to incentive systems,
  budgets and financial reporting
Forecast
desired
outcomes
possible
outcomes
leadership
“make it happen”
good
planning
Notes: Supply constraints examples:
Typical one: game consoles.
cars with hybrid engines;
flu vaccine in Fall 2004 was in short supply b/c one supplier in UK fell out.
iPod mini was supply constrained through Hitachi GST.
WSJ Europe Sep 21, 2007: Silicon shortage upends solar-panel makers
Technology changes over time! (Just like the cost of flat panel tv falls—more on this in Week 9 when we discuss process improvement and the learning curve.)
How did you represent your forecast and capture uncertainty?
Typical values of COV: staples (very stable) < 10%; 10-50% is typical (normal distribution works well); >100% is a lot; perhaps for new products (be careful to either truncate normal or use another distribution like gamma or so).
We showed three academic principles, but to what extend are these used in practice? (next 3 slides)
How estimate your standard deviation?
can’t do in Harly case, need a “reasonable guess”
should track A/F ratios and then set sigma = (sigma of A/F ratios) x point forecast
Scenario analysis:
  set up at least three scenarios (expected, best, worst) of demand evoluation.
  best: simulate thousands of scenarios automatically:
    - draw random paths yourself and use data tables in Excel
    - use a spreadsheet add-in such as At-Risk or Crystal Ball
    this is discussed in Sid’s spreadsheet elective.
Do explain other means of forecasts: goal setting etc. Very important!

## Slide 14: Financial Analysis of Capacity Strategy Valuation & NPV: Important Operations Elements
Forecasts of demand, supply and margins
Distinguish demand from output and sales!
Model capacity adjustments + continuous improvements
Include plans or options for model changes and future new products
Moving baseline: it is often easier to do two separate discounted cash flow analyses: 1. “do not invest” 2. “do invest” find NPV as their difference
Capture risk
Notes: Stress:
Do capture volatility somehow
Use same demand forecast to evaluate all 5 options! (unless you have a good story of why future demand depends on your capacity strategy chosen.) This means also using same time-horizon in NPV for all 5 options.
Time horizon should be more than 5 years, say 10, b/c o/w you don’t capture the upside of greenfield compared to brownfield. (it will take 5 years for brownfield to be fully utilized!)
CI is often forgotten…
How did you capture risk?
    Disaster scenario: require break-even
    Maximize expected NPV
    Consider option values of delaying/better information

## Slide 15: Tools to Incorporate risk into analysis:
Scenario Analysis (concurrent, discrete)
Decision Trees (sequential, discrete)
Simulation
Steps for Scenario Analysis:
Determine the factors you build around
Determine scenarios
Assign probabilities
Estimate cash flow for each scenario
Compute Expected NPV
Notes: Discuss this a little and then link to Seagate case where they should use this.
Decision analysis = decision trees (scenario analysis is a static decision tree)
When the Chileans worked on the rescue of the miners in 2011, they used decisions trees before making a decision on which action to pursue to rescue them and be prepared with the possible contingencies (air supply may be low; mine shaft may collapse, etc.)
Use this to remind them of the canonical model of risk in operations: newsvendor model, but now to decide on capacity (versus inventory).
1. Factor to build around: decide on capacity K, given fixed and variable investment cost (c_0 and c_K), and demand forecast and price.
2. Two scenarios: D > K, or not
3. Assign probabilities
4. Cash flow in each scenario
5. ENPV
“Use this approach for the Seagate case where now you focus on 3 discrete scenarios and a network investment (multiple capacities—some dedicated, others shared).
Solution is simplified by comparing the marginal value of a specific capacity number with its marginal cost.”

## Slide 16: Scenario Analysis
K
Decide
Capacity Size
V1(K)
p1
Contingent Value
X
Observe
Unknown
Probability
V2(K)
p2
V3(K)
p3

## Slide 17: Marginal Analysis and Newsvendor Solution

## Slide 18: Capacity Strategy: Sizing Summary
The concept of a capacity strategy
  Long range plan of capacity sizing/adjustment over time with decisions on capacity type/technology and location
Many factors to include. Special attention must be devoted to the role of uncertainty and risk
Tools to include risk:
  Scenario Analysis (concurrent, discrete)
  Decision Trees (sequential, discrete)
  Simulation

## Slide 19: Risk Management and Operational Hedging
What is risk? Likelihood x Consequences
  undesirable consequences of uncertainty
  Variance
  Two types of risk:
    Operational risk
      the threat that a resource, process, or system will fail to perform as intended
      the risk of a mismatch between supply and demand, which reduces expected profit flows
    Financial risk is about the undesirable variability of realized profit flows
What is risk management? Control likelihood or consequences
Hedging means mitigating these risks:
  Operational hedging are constructions in the operating system to reduce operational risks that may increase expected profits as well as reduce its variance
  Financial hedging are constructions with financial instruments to reduce the variance of profits
Notes: Nobody calls a likelihood of winning $1M a risk …
  Undesirable … = hazard x exposure = p x $loss
  Other measurements of risk:
    Expected downside loss, VaR, semivariances, …
    Utility. This boils down to using variance if:
    Exponential utility (downside weighs more than upside)
    Linear technology
    Normal forecast
What is operational risk: different interpretations
  1. Operational Risk is the threat that a resource, process, or system will fail to perform as intended
  2. mismatch risk
Differentiate mismatch risk (as in Seagate, which is expected profit difference) from profit variability risk
  How do you analyze risk? Easiest is decision trees, otherwise simulation
Operational hedging = configure the operational system for speed and flexibility so as to be resilient to risk
  Of disruption risk: P&G’s Pringles plant in Jackson, Tenessee, burns down but they quickly re-route production to the Belgian plant
  Of normal risk: flexible airline tickets or opaque tickets in Hotwire or Priceline
Financial hedging:
  P&G also has property insurance, one financial instrument to mitigate risk
  Porsche is very dependent on US sales so it hedges its currency exchange rate risk with futures and other derivatives
Rene Caldentey has a nice picture: There is correlation between financial markets and firm activities (say sales and sourcing). For example, exchange rates. Due to possible correlations I can use financial markets to:
  Get more information
  Reduce my risk

## Slide 20: Capacity as a Real Option: Value and Volatility
Capacity caps output and this non-linearity makes capacity valuation strongly dependent on demand volatility and on the impact of shortages
demand
output
capacity
1
1
capacity
0
0
demand
distribution
Notes: “What real options are imbedded in capacity?”
Discuss the kink: this is like a call option! It also shows that “capacity caps output”
  Capacity is a real call option in that we can choose to utilize it, but only up to a limit.
  Besides the call option, capacity also has several other imbedded options:
    The capacity timing decision has an associated option value of delay
    In a multi-product company, flexible resources have a switching or substitution option
    flexible and redundant capacity has an option to reduce risk (see later in global network)
Then get into volatility, which is key to capacity valuation. To see this, consider this simple example:
  assume first that we set capacity = mean demand.
  Explain capping by drawing output distribution: 50% mass point at K, and the rest goes through “unfiltered.”
  Net effect of increasing variability: more downside, no upside. When we increase capacity investment, the non-linear payoff function changes accordingly: the "kink" in the figure moves upward. The associated gain picks up less and less upside potential so that the associated marginal value of capacity investment typically shows diminishing returns, as we shall see shortly.
  Key Implication: If you disregard volatility, you overvalue capacity. Think about how to include volatility in your Harley case.
  The fact that the expected shortfall increases with volatility means that the marginal value of capacity depends on volatility. Typically, you will invest more as volatility increases = safety capacity.
Difference with financial options:
  Capacity is a durable good and can be exercised repeatedly
  Capacity time horizons are much longer
  Capacity options are about quantity constraints (not price constraints)
  With capacity more volatility degrades value.

## Slide 21: Capacity Sizing: Volatility & Safety Capacity
0%
2%
4%
6%
8%
10%
12%
0%
5%
10%
15%
20%
25%
30%
Demand Volatility
(Coefficient of variation)
Safety Capacity
0%
10%
20%
30%
Capacity Shortfall Rate
0%
0%
Volatility (COV)
Optimal Capacity Size
capacity K *
Safety Capacity
average capacity requirement R
100%
z *
Notes: You can analyze the intuition from the previous graph with a newsvendor model, similar to the way you analyze optimal safety stock where we saw in the core class: total stock = cycle stock (to fill average requirements) + z * sigma.
These graphs show the outcome of that analysis with normal demand.
Key insights:
Expected shortfall indeed increases in COV and safety capacity mitigates that
Optimal safety capacity depends on COV (linearly with normal demand if critical fractile > 0.5)
THUS: to evaluate capacity strategy, we must incorporate volatility/risk! Let discuss how you did that in Harley case!

## Slide 22: Contributions to ROIC increase, 1992-2007 (McKinsey)
Return Effect
Cost Effect
Sales Effect
Price Inc.
ROIC
Invested Capital Effect
Reduced investment Effect
Increased Capital Efficiency
Price increase without product improvement
New Product at existing facility
Product Improvement
New Product that requires extra capital investment
Output increase
Structural cost reductions
Reduction of Operating Cost
New or expanded capacity
Higher Utilization
Higher Productivity
100%
48%
25%
77%
23%
40%
14%
37%
11%
20%
7%
7%
3%
10%
11%
2%
7%
26%
11%
8%
15%
23%
Source: CapEx Excellence by Hansen, Huhn,
Legrand, Steiners, and Vahlenkamp.
2009, Wiley.
Notes: From CapEx Excellence book which reports on a specific McKinsey study that looked at S&P500 firms (and removed the financial firms) and correlated their ROIC with all kinds of factors.
Facts (not on this slide):
Investments are a core driver of economic growth worlwide: there is a 69% correlation between average investment rate over 1992-2007 and average real GDP growth. (although this is not cause effect!)
Over the past 20 years, companies have moved from profit maximization to value maximization: companies create value by investing capital at rates of return above their cost of capital. This new focus on ROIC apears to have had an effect as the median ROIC of S&P 500 has risen from 11% in 92 to 26% in 2007. “This is all the more remarkable since the recent ROIC increase has not been accompanied by an increased rate of growth in sales.” The difference between the 10-year moving average of revenue-weighted ROIC in 1992 and 2007 is 4.8%. Eliminating the structural change in the S&P 500 towards more asset-light industries (services, IT) and focusing on asset-heavy industries, we see a 3.8% ROIC delta.
McKinsey estimates that 48% of this 3.8% ROIC delta is investment related:
about one quart (23%) is driven directly by reductions in the level of invested capital relative to net profits. (bottom of slide)
About three-quarts (77%) derives from the groth in coprorate profits: either from cost improvement or revenue growth
[Here we see that, if there is an increase in ROIC (let’s call that 100%), then 48% of the increase is due to CapEx.
This can further be divided: 23% is direct capital effect and 77% (of the total 100%) is from return. From that 77%, 25% is due to Cap Ex, as indicated in green.
Etc….]
The bottom line is that, when you see an ROIC increase, on average, about half of that comes from CapEx.

## Slide 23: What is Productivity? Powertrains per 1000 hours worked
0
20
40
60
80
100
81
82
83
84
85
86
87
88
89
90
91
92
93
94
95
96
97
98
99
00
Year
Number of Powertrains
Notes: Unit per DL hour about doubled in 10 years. This corresponds to an annual productivity growth rate of 7%.

## Slide 24: Forecasting in Practice
Principle: Forecasts should include uncertainty by time bucket.
Challenges in practice:
Many companies use only point forecasts
Forecasts require cross-functional input and agreement
Most important: forecasts often serve other means:
  Goal setting, often connected to incentive systems
  Budgeting and financial reporting
Notes: How estimate your standard deviation?
can’t do in Harly case, need a “reasonable guess”
should track A/F ratios and then set sigma = (sigma of A/F ratios) x point forecast
Scenario analysis:
  set up at least three scenarios (expected, best, worst) of demand evoluation.
  best: simulate thousands of scenarios automatically:
    - draw random paths yourself and use data tables in Excel
    - use a spreadsheet add-in such as At-Risk or Crystal Ball
    this is discussed in Sid’s spreadsheet elective.
Do explain other means of forecasts: goal setting etc. Very important!