## Slide 1: PharmaFlex: NPV of Product-Specific Strategies (not risk-adjusted)
It is better to formulate a product-specific facility strategy:
  Calculate NPV for each facility strategy for each product
  Implement highest NPV facility strategy for each product
Summary result:
TABLE 1
Q:
  What is optimal strategy?
  What is the value of a product-specific strategy (ignoring risk for now)?
 | Gamma | Delta | Iota | "All" Strategy
Specialized | $53.15 | $26.23 | $0.28 | $79.66
Flexible | $(19.24) | $0.93 | $8.11 | $(6.52)
Transfer | $47.86 | $21.97 | $2.51 | $72.35
Notes: Key:
Alphatine = 16,000kg (1 rig)
Betazine = 4,000 kg (1/4 rig)
Clorazine = 1,000 kg (still needs ¼ rig specialized = at best 25% utilized!) It makes sense that flexibility enjoys the economies of scale here by having other products fill it up and avoiding the underutilization.
Recall: For not product-specific facility strategy:
If all products in spec = 72.28 + 18.07+18.07 = 108.42
The optimal product-specific strategy is to minimize PV by putting A and B in specialized, but C in Flexible (reason = volume!). The key insight here is that a MIXED strategy is better than all-specialized or all-flexible. This is answer to question 3: are there alternatives?
Result: total PV = 72.28 + 18.07 + 12.66 = $103.01M.
Thus: value of product-specific strategy = $108.42 – 103.01 = 18.07 – 12.66 = $5.41M
Note:
Sum of NPV of specialized = 72.28+18.07+18.07 = $108.07, as before
sum of all in flex here is larger than all in flex earlier b/c we assume here that cap constraints holds per product. Here were are producing more kg: 216,650kg vs. 184,975 in all flex.)
Sum of launch = $86.60+24.50+16.15= $127.25, as before

## Slide 2: PharmaFlex: Tailored flexibility strategy based on volume-specific and risk-adjusted evaluation of different options
Flex & Transfer
Flex & Transfer
Flexible Facility
Specialized
Specialized
Summary: Approval-risk adjusted facility strategy for Phase III start:
Gamma
Delta:
Iotae:
Pr{approval}
0%
100%
83.1%
60.4%
Notes: Key impact of risk: decision for Alphatine changes!
Recall that alpha is highest volume, betazine is medium, and chlorazine is low volume.
Stress that the summary really is a 2D strategy: risk on x-axis, product volume on y-axis.
Numbers for alphatine:
Specialized: EPV = 25 + p48.28
Flex: EPV = p 180.03
Launch: EPV = p 86.60
Again, launch dominates flex. Break p = 25/(86.60-48.28) = 64%
(The reason that 64% > 49% is not in line with what we would expect: it is not just volume that plays a role, but also the ratio of specialized capex to the difference of operating costs under specialized and launch. That is not so intuitive.) Launch delays CapEx, the value of which in NPV-terms increases with volume! (c.f. what we said earlier about value of waiting!)

## Slide 3: Learning Points: Capacity Types and Flexibility
Designing a capacity strategy includes:
  Sizing: for peak demand or risk loosing sales when no inventory smoothing
  Timing: when to build facility or transfer to other facilities
  Type: product-dedicated or flexible capacity?
Flexibility: typically cost is easy to measure whereas valuation is difficult and driven by:
  Scale: high volume suggests dedicated capacity, low volume flexible.
    Tool: volume threshold rule
  Risk: impact of timing of information and postponement to reduce risk.
    Tool: real options (abandonment/kill, expansion); waste factors
  Revenue maximization: switch to most profitable product + don’t be late
Capacity (technology & facility) strategy must be aligned with new product development:
  Align with anticipated volume, risk, and timing of new product introductions
Need to know value drivers
Notes: Bring in the discussion about “how to improve the T-C trade-off” of later slide. This is an answer to question 2: “how does flex fit with cost and time reduction?”
Stress that next case (Seagate) is about:
Capacity sizing for a capacity portfolio
Commercial (demand) risk

## Slide 4: Flexibility: How can we improve the Time-Cost trade-off ?
Improving the trade-off
  Depends on the capacity type strategy!
  How do this?
Impact on long-term capability building
  Different capacity types require different capabilities for improvement
  It also is useful to distinguish the two potential roles of the flex plant: low-volume plant or launch plant
Implementing a change in operations strategy: distinguish between short and long term implications:
  Flexibility may reduce integration and visibility; its benefits accrue mostly in the future
  Launch plant (mixed strategy) requires new capabilities
T (responsiveness)
C (cost efficiency)
Flex
facilities
Specialized
facilities
2
1
Notes: Next year: put this slide in after summary of flex valuation and types (as lead in to how to improve trade-offs)
How does flex fit with cost and time reduction?
role of flex plant: either as low-volume plant or as risk-mitigation (launch) plant
Improve trade-off:
if we go with flexible plants: must decrease cost of flex by:
  Technology change: Narrowing the band (adaptable, not completely flexible)
  Process improvement: Quicker changeovers (say to 1 week saves us 4 weeks = 8% utilization)
If we go with specialized plants: must decrease T by cutting critical path (project mgt improvement)
  Concurrent design and engineering
  Modular construction
Impact on LT capabilities: flexible plants require process improvement skills, whereas specialized plants require cross-functional project improvement skills. VERY DIFFERENT.

## Slide 5: Capacity Timing and Types Guidelines for speed and flexibility
Streamline project management
  Work in parallel + do activities independent of timing and sizing in advance
    Use design/build partners
  Eliminate activities and reduce activity times and rework
    Use standard designs or re-use previous designs
Plan for Uncertainty
  Modularize capacity and construction
  Increase adjustment flexibility
    Reduce chunks, investment (commitment) or increase resale
  Adapt and postpone capacity
    Keep initial scope simple
    Include options for adjustment later
      Use adaptable, flexible, or “smart” capacity
Notes: Which frictions to these actions attack?
Cut capacity leadtime
Reduce lumpiness (and thus also leadtime)
Reduce irreversibility
Reduce uncertainty
Who’s got experience with any of these actions?
Project mgt: action 1 decrease critical path; action 2 reduces actual activity times, eliminates activities and reduces rework.
Use proven “standardized” designs
As obvious as this is to reducing costs, decreasing time, and having predictable outcomes… it is very difficult to accomplish culturally. People always want to build new and think they can do it better.
This is similar to teaching: new faculty are encouraged to follow standard optimized course but often they like to try it their way…
Modularize: challenge is to create incremental capacity quickly with little premium to larger chunks = minimize impact of EoS
one approach may be to commit with a vendor to multiple modules with adjustable future deliveries
Key: first two actions focus on time, the other two on flexibility
They can be used in combination

## Slide 6: “Include options for adjustment later”: Real Options = Contingent Expansion Planning at Hong Kong Disneyland
Built small in 2003 with standard 4 themed areas:
  Main Street, Adventureland, Fantasyland and Tomorrowland.
Strategy = expand as demand grows
2009: add 3 on perimeter
2016: expand Tomorrowland
Harley-Davidson calls these expansion times “triggers”
Notes: From: Benne Nathaniel Rosner <brosner2016@kellogg.northwestern.edu>
Date: Tuesday, February 2, 2016 at 12:33 PM
To: Jan Van Mieghem <vanmieghem@kellogg.northwestern.edu>
Subject: Disney Theme Park Capacity Planning
Hi Professor Van Mieghem,
I wanted to follow up quickly with an example from Disney Theme Parks on capacity planning. When Hong Kong Disneyland was built in 2003, it consisted of standard 4 themed areas: Main Street, Adventureland, Fantasyland and Tomorrowland.
[if !supportLists]· [endif]The strategy was to build smaller but then expand as attendance grew over time.
[if !supportLists]· [endif]Consequently in 2009, they added three themed areas to the perimeter of the existing park: Toy Story Land, Grizzly Gulch and Mystic Point (site map attached with expansion areas in the top left corner).
[if !supportLists]· [endif]Now in 2016, an expansion of Tomorrowland to add in an “Iron Man Experience” ride, themed area and restaurant is being constructed.
This is one example of how Disney plans out capacity for its theme parks. While the magnitude of how small to start and how fast to expand has had some debate, the general idea of adding in future expansions to add capacity as demand grows is the same. Ultimately demand will grow such that the 1st theme park has reached its full capacity (all land parcels utilized), which is when we start working on adding a 2nd theme park to the site. Examples of this are:
[if !supportLists]· [endif]Adding Tokyo DisneySea to Tokyo Disneyland in Tokyo
[if !supportLists]· [endif]Adding Disney’s California Adventure to Disneyland in Anaheim, CA
[if !supportLists]· [endif]Adding EPCOT, Hollywood Studios and Animal Kingdom to Magic Kingdom in Orlando, FL
[if !supportLists]· [endif]Adding Walt Disney Studios Park to Disneyland Paris in Paris
Best,
Benne

## Slide 7: A Flexible Asset strategy should strive for cost reduction e.g. limit scope or speed up changeovers
Bill Fox (Lilly): “Flexibility with automation in a cGMP environment can be very expensive (and take a long time to build/validate)”
Capital
Investment
(CapEx $)
Agility flexibility or product changeover time
Dedicated
Flexible
with Automation
Adaptable
Days
Months
Quarters
0
0
Scope flexibility
Scale flexibility
Notes: In the Lilly case, there only was a choice between extremes. In reality, flexibility really is a spectrum: it depends on changeover times. In other words: scope-flexibility and agility are interdependent.
An adaptable facility:
is like a dedicated but with an additional set of piping/tooling etc that can cover most (but not all) other product requirements and can be reconfigured quickly for another product.
reduces the cost of flex by reducing the set of scenarios (parameter ranges) covered but staying adaptable.
Good Manufacturing Practice is a set of regulations, codes, and guidelines for the manufacture of drug substances (also known as active pharmaceutical ingredients (APIs)) and drug products (known as medicinal products in Europe), medical devices, in vivo and in vitro diagnostic products, and foods. In the United States GMPs are referred to as "cGMPs" or "current Good Manufacturing Practices" GMP is a term that is recognised worldwide for the control and management of manufacturing and quality control testing of pharmaceutical products.
GMPs are enforced in the United States by the FDA (Food and Drug Administration);

## Slide 8: A Specialized Asset strategy should reduce leadtime e.g. modular capacity and construction, concurrent design/build
Leading module manufacturer for pharma industry
Started in 1986
Swedish company
Provide modules to multiple industries
Lilly’s exclusive provider of modular construction
First factory in 1991
Egypt insulin facility world record time (12 months!)
Who is Pharmadule?
Lilly & Pharmadule
Ireland
Notes: Background on modular:
Building with modules has been going on ever since the start of the Industrial revolution:
  It combines “pre-build or pre-fabricated” in little chunks
Nearly all modules are produced with lightweight techniques, nowadays and before
Modular builders turn to a market of fast changing decisions
Modular buildings are used for many purposes
  Schools, day nurseries, offices, health care centers, service buildings, multi-family houses, single-family houses, hotels, industrial buildings, offshore modules, process buildings etc
NYT 2007: there is now an increase of modular construction for home in New Orleans after Hurrican Katrina
IF TIME: show from 2:25 to 3:10.
2012: “We did 20 modular construction facilities with Pharmadule (Sweden & N. Carolina). Biggest one about $1B in Puerto Rico. We no longer do that b/c later re-purposing is very difficult.”
“Using desing/build partners saves us about 3 months (not going through competitive bidding) but it may not give you the best price.”
For the case study, we chose an “adaptable facility”; actual cost was $10MM, time 1.5 years.

## Slide 9: Value of Flexibility in Auto Industry
Ford adjusted primarily by increasing
Ford EDGE
Manufactured in Oakville, ON (Inflexible plant)
Honda PILOT
Manufactured in Lincoln, AL
Alliston 2, ON
(Flexible plants)
Average incentive for flexible in 2007: $2,691
Average incentive for inflexible in 2007: $3,411

## Slide 10: How do firms use pricing and production flexibility to adjust to changes in demand?
Auto companies spent $28 billion in incentives in 2009
Costs of production flexibility are available to firms, but benefits of production flexibility harder to quantify
Moreno & Terwiesch empirical study:
  Vehicles marketed in the U.S.
  Period 2002-2009
  348 models, 20,052 model-month observations
Findings
Deployment of flexibility associated with:
- Reduction of incentives ($200-$700 per car)
- Increase in list prices
- Increase in utilization
Demand volatility associated to higher incentives

## Slide 11: Some thoughts on “how is the class going”

## Slide 12
Operations Strategy
Location and Global Networks
Location, Global Networks and Offshoring
  Integrate location decisions with operations strategy and globalization
  Four types of location analysis + concept of total landed cost
Notes: Let us now focus on location decisions.
This is directly relevant to the process of globalization—so to put things in perspective, consider the typical drivers in globalization. We’ll see that those directly miror decisions in our framework.
2011 Instructors: For location: two options—I will go with option 2:
  Do the stuff as in the slides (like 2 years ago): benefit is higher level overview of various methods
  Only do geographical analysis, leading to TLC, and follow this directly by the “blue slides” (the intro to Mex China): benefit is closer link-up and setup for the game (including how to calculate the order up to level under periodic ordering)

## Slide 14: First U.S. Assembly Plant for China’s Lenovo Opens in N.C.
Notes: http://www.npr.org/2013/06/06/189057722/lenovo-holds-grand-opening-for-its-n-c-assembly-plant?sc=tw&cc=share

## Slide 15: After decades of sending work across the world, companies are rethinking their offshoring strategies
The Economist, Jan 19th 2013

## Slide 16: Offshoring – is the honeymoon over?
“The growing need for lean inventories puts China at a disadvantage”
“Goods take 45 days on average to reach U.S. shores. With the recession making it more difficult to predict demand, manufacturers are being forced to stash unsold products in warehouses for longer periods. And the cost of meeting emergency supply needs is inevitably higher in China …”
So Much for the Cheap 'China Price’
  “In 2005 … by the time the items had arrived at a U.S. port, Chinese-made parts were 22% cheaper on average than those produced in the U.S. By the end of 2008, however, the average price gap had dropped to 5.5% ...”
  “All over China, wages are climbing at 15 to 20 percent a year because of the supply-and-demand imbalance for skilled labor,” said Harold L. Sirkin, a BCG senior partner. “We expect net labor costs for manufacturing in China and the U.S. to converge by around 2015. As a result of the changing economics, you’re going to see a lot more products ‘Made in the USA’ in the next five years.”
“Due to increased demand fluctuations, sourcing closer to home wins over other lower cost options overseas”
“… buy a harness from China for 15% less than in Mexico. But if a design is altered after a batch of Chinese-made harnesses is already on the boat from Shanghai, the company has to foot the bill for up to six weeks of shipping and handling of obsolete parts.“
Notes: There appear to be increasing forces slowing down offshoring...
But this doesn’t mean we should completely reverse to onshoring.
Global dual sourcing is a possibility, but this strategy comes with some challenges in itself (next slide)

## Slide 17: So much for the cheap “China price”: data
Manufacturing costs rose from 2004 to 2014 in most of the top 25 exporting countries. Some that are usually thought of as cheap places to produce goods like Russia, Taiwan and China now have costs pretty close to those in the United States.
Source: New York Times, Aug 2, 2015
Notes: http://www.nytimes.com/interactive/2015/07/31/business/international/rising-cost-of-manufacturing.html

## Slide 18: Global total cost comparison for making yarn
Although labor costs are relatively low in China, other costs like the price of raw materials and electricity have made it more expensive to make yarn there than in many other countries, including the United States.

## Slide 19: Capacity Location Globalization and operations
Market Demand Factors
Technological Factors
Supply Factors
Macroeconomic and Non-Market factors
Globalization
Process
•
Foreign demand growth
•
Foreign competition
•
C
ompetitive threat/priorities
•
State
-
of
-
the
-
art markets
•
Access to knowledge & skills
•
Infrastructure
•
IT: Network planning and coordination
•
Direct labor v. total
costs
•
Capital investments
& economies of scale
•
Taxes and incentives
•
Tariffs, quotas and other protectionism
•
Trade and global institutional agreements
•
Exchange rates
•
Political stability
Kouvelis and Niederhoff (2007)
Notes: Ask: which factors explain Goldwind’s locating in the US?
TAXES and INCENTIVES often play a HUGE role.
These are the typical factor to consider in global locations; they can be used to find opportunities for globalization.
Example: Toyota makes cars in China & US. Where should it make engines?
- local dedicated (‘onshore’)
- centralized (either US or China)
- global integrated network
Let’s integrate these factors with the drivers of operations strategy (next slide)

## Slide 20: Globalization at Bekaert
Source:
Annual Report 2012

## Slide 21: Globalization at Bekaert: Complete reversal in 15 years…
Source: Annual Report 2012

## Slide 22: Mini-Case: Mexico-China?
You are a $10B high-tech US manufacturer of wireless transmission components, about 20SKUs. Intense global competition put pressure on margins and working capital
You have two assembly plants, one in China and another in Mexico, that supply a warehouse in McAllen, TX.
How can you best manage this existing global network?
Notes: Emphasize that you have an existing global network (or at least have the option to change already identified locations. We shall not discuss how to find locations and related setup costs.)
The two key questions we want to address: you may have an existing SKU that is:
1. offshored to a low cost location; should you bring it back?
2. sourced locally; should you offshore it?
Or you may have a new SKU in the pipeline…
A good tool to analyze those decisions is TLC—how many of you found it better to use China for the SKUs in mini-case 6? How did you compute TLC?

## Slide 23: Global dual sourcing is a challenge for many companies
Demand Volatility
Supply Risk
What product and customer traits drive demand fluctuations?
How can sourcing decisions be tailored in light of shifting demand patterns?
What are the hard and soft costs of supply chain risk?
How can sourcing be responsive to mitigate risk?
Execution Complexity
How do I make product to plant allocation decisions?
What criteria should drive those decisions?
Cost Visibility
What are the hidden costs of global sourcing?
How can my total landed cost be determined?

## Slide 24: Total Landed Cost (TLC) Analysis
TLC = total supply chain cost from origin to destination for a given service level
TLC analysis enables improved business decisions without sacrificing customer service
  Where to procure goods?
  Where and how to deploy assets?
  How to allocate resources to optimize costs?
  How to optimize transportation services?
68%
9%
7%
8%
3%
3%
2%
100%
Total Landed Cost Breakdown
Illustrative
Typical COGS
Supply Chain
+ Service
Working Capital Costs
Notes: TLC = used for B2B (sourcing)
Cost to serve = used for B2C
You want to carefully track direct and indirect and hidden costs through the entire value chain. This analysis is painful (because that data is not always easy to find) but rewarding.
A manufacturer of cell phone transmission towers found that:
- often labor is not that significant
- but sourcing and working capital implications are.

## Slide 25: Global Networks: Total Landed Cost
TLC = total end-to-end cost to transform inputs at sourcing location to outputs at customer locations
Track flow units through the process (ABC-like): e.g. offshoring
  Inbound RM and services purchased at offshore plant
  Inbound logistics of moving inputs to offshore plant
  Processing and inventory cost at offshore plant
  OH at offshore plant and domestically
  Logistics from offshore plant to domestic DC: consider cost and leadtimes for
    Offshore plant > offshore port > domestic port > DC
    Consider working capital (both cash cost and pipeline inventory)
  Outbound fulfillment from DC
    Consider cycle and safety stock and outbound transportation
  Include any other costs that are impacted by increased activity in end-to-end
Key for Mexico China
Dual Sourcing Simulation
Notes: You’ll need this for Mini-Case 6.
A. Some additions to Mini-Case 6 questions to keep things specific:
For all questions: focus on the TLC to supply North America only. Furthermore:
For question 1: Contrast the TLC assuming all products are produced in Mexico or all in China. For China, assume % of shipments by sea = 100%, 50%, and 0%. (In other words: calculate four TLC numbers.)
For question 2: Now implement the proposed tailored global operations strategy and assume first that “high volume” means “monthly sales exceed 30,000 units.” (Thus, the four top SKUs are dual sourced: China serves the base demand of the top 4 SKUs while Mexico serves their surge demand. The remaining SKUs are single sourced from Mexico.) How does TLC depend on the choice of what “high volume” means? How do you suggest implementing a tailored global strategy? B. The case data and an addendum written by Deloitte are downloadable from BlackBoard under "Course Materials>Case Data". C. For section 62, you can follow the syllabus' instructions for your group number - 20. (Section 62 group numbers start from 21, so group 24 is equivalent to group 4 for the purpose of this assignment.)

## Slide 26: Working capital includes inventory. Review: Inventory has several components
In-transit stock = (avg. throughput) x (avg. transportation time)
Cycle stock = Q/2 = from recurrent batch deliveries of size Q
Safety stock
mean
demand during
“at risk” period
Stock-out probability
Cycle Service Level (CSL)
Is = z s
0
z
Notes: Note:
Later in the game we will have:
Sigma = 15
What should service level be? Two bounds:
Simple single-period newsboy suggests optimal service level = (p-c)/p = about $3/$10 = .3 so that z = -0.5
But we have inventory carry-over, so c is really only the holding cost so that SL = (10 - .07)/10 = 99% so that z = 2.45
This would set
Mexico safety stock at 2.45*15 = 36.8
China safety stock at 2.45*sqrt(4)*15 = 73.5

## Slide 27: Dynamic Inventory Control using Order-Up-To policy A: Leadtime L = 1
Stock-out probability
In-Stock probability
= Cycle Service Level (CSL)
Order-Up-to-Level OUL = mean + safety stock
Inventory
on-hand
Time t
0

## Slide 28: Dynamic Inventory Control using Order-Up-To policy B: Leadtime L > 1: Must include in-transit inventory
Stock-out probability
In-Stock probability
= Cycle Service Level (CSL)
Order-Up-to-Level OUL = mean + safety stock
Inventory
on-hand
+
in-transit
Time t
0
Leadtime-Demand distribution:
mean = L x meanperiod
Stdev = sqrt(L) x stdevperiod

## Slide 29: Review: Computing pipleline + safety stock for LEX 100021: single sourcing from Mexico
Leadtime L = 8.5 days = 0.28 months
In-transit inventory = 67,200 units/mo x 0.28mo = 19,040 units
Safety stock = z sqrt(L) sR = 1.65 * sqrt(0.28) * 20,160 = 17,651 units
Cost:
  COGS from Mex = $608.73/unit
  Unit holding cost = 15%/year * $608.73 = $91.31/year = $7.61/month
  Monthly carrying cost = (19,040+17,651) * $7.61 = $279,184
Depends on your targeted SL
e.g., if 95%, then z = normsinv(.95) = 1.65

## Slide 30: Digital Supply Networks
Join Us
Thursday, March 1, 2018 12:15 p.m. – 1:15 p.m.
KGH - 1420
Presented By
Stephen Laaper Principal, Deloitte Consulting
Copyright © 2017 Deloitte Development LLC. All rights reserved.
Hear from the leader of Deloitte’s Digital Supply Networks practice, Stephen Laaper, as he discusses how these dynamic, interconnected systems are different from the traditional supply chain.
Stay after the event to interact with a VR demo!1
Want to learn about how digital technologies are disrupting the way modern supply chains work?
Join us to learn about Deloitte’s point of view on Digital Supply Networks and how we helped a client train employees using Virtual Reality (VR)!
Click HERE to register!
1. Demo trials available from 1:30 to 2:30 pm and subject to capacity limitations

## Slide 31: Location Strategy Framework
How do we identify alternative global supply markets for now and institutionalize the capability to do so again in the future?
Notes: Proxima (American Standard or Moen?) was one of the first American household products (faucets/plumbing) manufacturers that went to China.
The company enjoyed the first-mover’s advantage by setting up shop in China during the late eighties before many of its competitors did. 20 years later:
The market tanked in 08-09
2. China’s rapid growth, however, is increasing direct material costs through inflation of wages and producer prices.
Proxima is expecting a squeeze on profit due to increase in costs from China’s supply base and wants to evaluate whether other markets offer a new first mover advantage.
Facts:
Proxima has over 100 unique suppliers and its supply base is highly concentrated: 35% US and over 65% of their raw materials arriving from just a few suppliers. Two of those core (Chinese) suppliers are expected to go bankrupt…unless they increase their price to Proxima. Developing an alternate supply base for Proxima’s raw materials typically takes about 2-3 years.
China’s growth over the last decade has led to ~10% year-over-year cost inflation in wages and producer prices, leading to increased sourcing costs for companies like Proxima. A four-year projection of the cost baseline reveals an estimated cost increase by ~50%.
Component costs, including factors such as raw material, labor, overhead and finishing costs, make up 67% of the total product costs for Proxima. Final assembly and packing are the next highest cost components, at 13% and 7% of total product costs, respectively.
KEY INSIGHT: We cannot stay in China: “Who is the next China?”

## Slide 32: Step 1: Strategic role of a foreign location
Adapted from Ferdows (1997) “Making the most of foreign factories. HBR, Mar-Apr, 73-88.
Source plant
•
Produces at low cost but with same
ability as best plant in the network
•
Authority over procurement, production
planning, logistics, process & product
customization
Offshore plant
•
Produces specific items at low cost
and exports for further work or for sale.
•
Minimal authority and investment.
Lead plant
•
Global hub for product and process
knowledge and innovation.
•
Full authority over all activities. Taps
into local skills and knowledge to
initiate company
-
wide innovation.
Outpost plant
•
Primary role is to collect information
from advanced suppliers, competitors,
research labs, or customers.
•
Secondary role as offshore or server.
Server plant
•
Serves specific regional market to
overcome tariffs, taxes, logistics, or
foreign
-
exchange risk.
•
Limited authority to make minor
modifications to fit local conditions.
Contributor plant
•
Serves specific regional market but
competes with other plants in network
for new processes or products.
•
Authority over product and process
development as well as supplier choice.
What is the primary strategic reason for the location?
Access to low
-
cost production
Access to skills and knowledge
Access to market
Narrow & low
Broad & high
What is the scope of its current
activities and competencies?
Notes: Last type of analysis:
strategic or focus/role of a location: matrix considers two dimensions:
What is primary strategic reason of the location?
What are its scope and competencies?
The traditional (old-fashioned) reasons for foreign locations were narrow in scope (lower row)
ALMOST every foreign plant starts in the lower row.
Do you know examples?
- offshoring = Cortina shoes
- outpost = Canon research center Palo Alo
server = Coca Cola bottling plants; Kellogg MIA
utpost + server = BMW in US; Toyota in Valenciennes, France.
True global networks move locations to the upper row: it can take a long time to move toward middle and upper boxes!
Lead plants = at the top of the pyramid in terms of strategic role
A printer company that puts R&D and mfg together but for components: so one location on IC boards, another power supplies, a third cartridges and toner, etc.
HP singapore = lead for keyboards and inkjet printers
McK has various centers of competence around the world

## Slide 33: Step 2: Global Assessment of industry presence > set of candidate locations
Notes: KEY: It is a lot of work to analyze all relevant location factors for all countries > Use a hierarchical approach:
How can you select out of 200 countries?
Start with global trade export screening: using SIC codes; e.g. chrome coating
Select 20 countries by country attractiveness assessment
Select 13 countries by cost evaluation using TLC
Narrow down to 3-6 countries.

## Slide 34: Step 3: Country segmentation > set of attractive candidate locations
Notes: Start with elimination factors:
High cost countries (e.g. Germany)
Economic treaties
Availability of raw material
Service level: can I get there in 2 weeks?
Using the export data, 20 countries were retained. Those were then scored on Technical x Business. (next slide puts them in a map)
KEY: there are many factors to consider, some don’t matter, some have more weight. It is an iterative process where you must include all stakeholders (functions inside the company, board, etc.)
Where do you get the data?
Google
CIA factbook
Economic data you can buy
Get local info from local consultant offices (Deloitte local offices + it has an internal Deloitte practice doing this)
Out of 20 countries, 13 were retained as candidates. For those 13, now do all the works and establish TLC.
The weighted sum (line) can be changed depending on preferences of executives.

## Slide 35: Step 4: Total Landed Cost (TLC) Analysis
TLC = total supply chain cost from origin to destination for a given service level
TLC analysis enables improved business decisions without sacrificing customer service
  Where to procure goods?
  Where and how to deploy assets?
  How to allocate resources to optimize costs?
  How to optimize transportation services?
68%
9%
7%
8%
3%
3%
2%
100%
Total Landed Cost Breakdown
Illustrative
Typical COGS
Supply Chain
+ Service
Working Capital Costs
Notes: TLC = used for B2B (sourcing)
Cost to serve = used for B2C
You want to carefully track direct and indirect and hidden costs through the entire value chain. This analysis is painful (because that data is not always easy to find) but rewarding.
A manufacturer of cell phone transmission towers found that:
- often labor is not that significant
- but sourcing and working capital implications are.

## Slide 36: TLC in Apparel: Bayard Winthrop, founder of American Giant
Source: New York Times, Sep 20, 2013

## Slide 37: Service - Location Tradeoffs
100%
TLC
Safety stock holding cost
Service Level (in-stock probability)
Offshore
Nearshore
50%
0
TLCnearshore
TLCoffshore

## Slide 38: Step 5: Dynamic Updating provides dynamic location recommendation
2014 2015 2016 2017 2018
Notes: Q: why not start with TLC first and then do the qualitatives?
A: We would do that for tactical sourcing + TLC takes too much work to do for all countries.

## Slide 39: “The Robots Are Coming for Garment Workers. That’s Good for the U.S., Bad for Poor Countries”*
From 2000 to 2010, Bangladeshi garment exports nearly tripled, helping to dramatically push down the number of people living in poverty, the World Bank says. Many were women from poor rural areas who migrated to the cities, including Dhaka, and sent earnings home. Today the industry provides three million manufacturing jobs and 81% of Bangladesh’s exports.
* Wall Street Journal, Feb 16, 2018

## Slide 40: Location Decision Tools to keep in mind
Strategic facility role matrix (see earlier)
Geographical or spatial analysis of global network
  Timing and location decisions may interact
  Geographical or spatial analysis includes TLS for one location or for all locations in your network
Competitive analysis
  Hoteling location model
Notes: Let’s summarize four typical types of location analysis.
Spatial: typically TLC for one location: example = Mex-China mini-case
Network: considers total costs for ALL locations in the network: example = capstone case
Competitive analysis: famous Hoteling model that you’ve covered elsewhere….
Facility role: see matrix

## Slide 41: Capacity Location: Network analysis Capacity timing and location interact
A
C
B
http://nationalatlas.gov/
Notes: Timing and lcoation also interact.
You are Acciona and are starting operations in the US.
- Assume you have a myopic view and build one location: that would be best in A.
- If, however, you anticipate potential future additions: it may be better to start in B so that in the longer term you add C. [B+C have lower TLC than A.]

## Slide 42: Capacity Location: Spatial analysis Poppies Int’l
5%
7%
20%
27%
25%
16%
St. Louis
2063 miles
1840 miles
640 miles
555 miles
960 miles
300 miles
Notes: For which industries is spatial analysis important?
- when transportation is an important cost factor

## Slide 43: US major purchasers for a white goods appliance manufacturer
Notes: Professor,
Attached is the image I showed you after class displaying product distribution across the US for a major appliance manufacturer. Again, my client used this map along with other information to make decisions about where to offer premium service operations. Please feel free to share this with the class as long as we keep the name of the company confidential.
Cheers,
Michael Loesel
________________________________________________
Michael D. Loesel
mloesel2007@kellogg.northwestern.edu
Kellogg School of Management
Northwestern University
Many costs exhibit EoS, but outbound transportation does not.
How does Amazon decide on the size and location of DCs?

## Slide 44: Capacity Location: Network analysis Should a network be centralized or distributed?
Size of area served
by one location
Cost
per unit
Costs with increasing returns
to scale (e.g., capacity, inventory)
Costs with decreasing
returns to scale (e.g. transportation)
Total cost (sum)
Economically optimal
size of area served
from one location
Distributed network
Centralized network
0
0
Capacity sizing and location are interdependent!
Notes: Many costs exhibit EoS, but outbound transportation does not.
How does Amazon decide on the size and location of DCs?

## Slide 45
Notes: One of my favorite data-maps is a well known piece by Stephen Von Worley: The Contiguous United States Visualized by Distance to the Nearest McDonalds.
The furthest you can get within the USA is ~107 miles, incidentally. It's a brilliant post; fun, personal, and on a subtle level is discussing a deep part of Americana.

## Slide 46: The United States of Starbucks
www.ifweassume.com/2012/10/the-united-states-of-starbucks.html
http://www.boston.com/yourtown/massfacts/snapshot_dunkin_donuts_vs_starbucks_massachusetts/
Notes: http://www.ifweassume.com/2012/10/the-united-states-of-starbucks.html
Another chain restaurant by which we might measure our lives, particularly in the PNW, isStarbucks. This Seattle-based-behemoth has played an integral role in the coffee culture around the world, and along with the Nerd Triumvirate (Microsoft, Boeing, and Amazon) has secured our city's place on the global stage. Starbucks has been used in the past to gauge economic health, and I've found it used as a standard metric in geography classes. The closer you live to a Starbucks the higher your rent is likely to be, and in NYC the density of locations can reach as high as 150 with a radius of 5 miles! I wanted to look at not only how Starbucks were distributed across the USA (like in Von Worley's McMasterpiece) but how we are distributed around Starbucks. Here is the USA as mapped by Starbucks-owned locations (with thanks to my friend David B), connected using a Delaunay triangulation. As with Mc D's, these latte-slingers are clustered around major cities and highways. As an aside, I wonder if anyone has tried to calculate the optimal path for visiting every location...
Related to the Delaunay triangulation, here is the Voronoi diagram for every Starbucks location. This beautiful grid of spaces can be used to tell you the furthest point from a company-owned Starbucks (about 170miles 140miles, though note that other franchise locations are relatively nearby, e.g. inside of grocery stores)
Finally: by comparing Starbucks locations to everyone's favorite data source (the US 2010 Census) we can make a graph with a truly impressive result (in my opinion). By counting the number of people who live within a given distance to each Starbucks, we can measure how well centered Frappuccinos are to the US citizenry. In other words: draw a 1-mile circle around every store, then add up the % of the population living within the circles. Repeat for 2, 3, 4....100 miles. What I found left my jaw hanging...
There are ~311 million people living in the USA, with 82% living in urbanized areas. One might define urbanization in the modern era as the distance to the nearest Starbucks. An "urban" environment would therefore be anyplace within a 20 mile radius. Yes, more than 80% of the USA (that's 250,000,000 people) live within 20 miles of a Starbucks. While it might seem silly to drive 20 miles for a cup of Pike Place Roast, you would definitely drive that far to Lowes or Costco or Ikea... and you might get thirsty while you're out! And thus the burr grinder of progress spins on.
Professor Van Mieghem,
Here is a fun diagram showing the network distributions for both Starbucks and Dunkin Donuts in my home state (Massachusetts). It’s a little dated but it does a good job of representing why Starbucks has struggled to enter this market.
http://www.boston.com/yourtown/massfacts/snapshot_dunkin_donuts_vs_starbucks_massachusetts/
Best,
Sam
--
Sam Shepard

## Slide 47: Learning Points
Capacity Location:
  Location decisions should be integrated with the entire operations strategy. They also explain the forces behind globalization.
  Strategic location analysis:
    Strategic role analysis  Offshoring
    Global assessment  candidate locations
    Country segmentation  attractive candidate locations
    Geographic, spatial network analysis  TLC
      Should networks be centralized or distributed? Optimal size of a location
      Competitive analysis
    Dynamic updating
Notes:     Next Case: Mexico-China + panel

## Slide 48
Operations Strategy (week 7)
Global Dual Sourcing and Offshoring
Strategic global sourcing allocation
  Principles from research
  Lessons and guidelines from practice
    Simulation Game and Case: Mexico-China
Notes: Ex-post plan for 1.5hour, Feb 07, 2011 class:
All students have prepared as mini-case the spreadsheet assignment, so we’re all ready to start playing the game immediately without any further intro.
In previous class (and I will also put it in the syllabus next time) I told them:
Come to class with two laptops per team and sit by team. Both laptops should have Firefox and the Excel spreadsheet.
BRING BACKUP SHEETS AND BACKUP EXCEL FILE
BRING one sheet for each team with their team name and password
BRING MY LAPTOP and use “extended screen”. Open two browsers: in one window (my private screen I set intervals and advance); after 4 periods (not earlier, so they cannot infer what each team is ordering during startup) I move the second window /status to the projector screen so all teams can see each other’s bank status.
ON BOARD:
Open http://tuck.sourcinggame.net in Mozilla Firefox
“SIT WITH YOUR TEAM.”
“ASK ME FOR TEAM NAME AND PASSWORD IF I HAVEN’T GIVEN YOU ONE YET.”
“WHEN PLAYING THE GAME DO NOT HIT ENTER AFTER TYPING IN ORDER. WAIT UNTIL ORDER FOR BOTH MEXICO AND CHINA ENTERED AND THEN HIT SUBMIT.”
“DO NOT CLICK ON RESULTS STATUS – I WILL SHOW THAT ON THE SCREEN.”
Note to me: If a student clicks on results status and doesn’t have adobe flash 6 it will want to download and then have to close firefox. If it happens, tell student to hit the back button.
Executed timing plan by JVM with 64 students/13 teams:
3:30-3:41: Started class with midterm evaluation feedback (at least 5min) & then start up game.
3:42: place order 1. NEXT TIME: do take some time here to explain how to read the web table and correspond with the Excel table. (I didn’t do this and one team told me they only figured it out in round 20.)
Start timer at 180 in round 5.
3:51: round 8. Timer to 100sec.
3:55: round 10: Timer to 60.
4:06: round 21: Timer to 50.
4:10: round 25: Timer to 45.
4:13: round 30: Timer to 40.
4:23: round 44: game over!
Debrief: show summary data and ask teams what they did.
Show forecasting and ask what they did (pick up dynamic strategies)
Slides in last 10 minutes—next time use 15.
Total 93min.
After class note from Brian Tomlin: timing went almost exactly as above, but got game started at about 8 minute mark. Could have spent more time on student debrief but wanted to cover slides. Students had a variety of strategies but quite a few had some flavor of base-surge. Key is to start giving team names out once more than one team member is present. I had team name and password written on index cards in advance and just handed a team member the card.
Plan for 3hour, Feb 03, 2009 class:
6:30-6:50pm: intro + TLC of single sourcing
6:50-8:00pm: Mexico-China game
15min break
8:15pm-8:50pm: debrief + research principles
8:50pm-9:30pm: Deloitte consultants.

## Slide 49: Simulation: Mexico-China?
You are a $10B high-tech US manufacturer of wireless transmission components. Global competition put pressure on margins and working capital
You have two assembly plants, one in China and another in Mexico, that supply a warehouse in McAllen, TX.
How can you best manage this existing global network? For simplicity, we will manage only 1 SKU and only sell to 1 market.
Notes: Emphasize that you have an existing global network (or at least have the option to change already identified locations. We shall not discuss how to find locations and related setup costs.)
The two key questions we want to address: you may have an existing SKU that is:
1. offshored to a low cost location; should you bring it back?
2. sourced locally; should you offshore it?

## Slide 50: Group numbers

## Slide 51: Group numbers

## Slide 52: Before we get started
Has every team received their team name, password, and backup sheet?
You can log on now (if you haven’t already).
  But don’t do anything yet (i.e., don’t submit any orders)
You must record your orders each period on the backup sheet.
  You can also use the spreadsheet offline if you want.

## Slide 53: Before we get started
Each period you need to place an order from China and from Mexico (an order can be 0; blank means 0).
DO NOT HIT ENTER after typing in one order. First type in orders for both Mexico and China and then hit submit.
  Once game is on a timer, order must be submitted before timer counts down. Otherwise, orders are both 0.

## Slide 54: Let’s start

## Slide 56: General Rationale for Offshoring
Pro
Con
Cost reductions
Proximity to local or new markets
Domestic labor market constraints
Operational hedge
Foreign trade barriers
Transportation costs
Lead times
Risks
  Quality, including health, environmental and CSR
  Currency, IP, political, competitive
Domestic trade barriers
Global operations’ complexity and social implications
The percentage of 2006 survey participants that cite the goals listed as a reason for offshoring.

## Slide 57: Capacity Location interacts with Sizing and Timing CargoLifter AG
The CargoLifter hangar in Brand, Germany
Notes: Hi Prof. v. Mieghem: You asked me to send you a story I brought up last class. When we talked about the Cargolifter Zeppelins, you asked me to talk about this company. My association with Cargolifter was that the unions at Audi were afraid of it. They thought that as long as VW invested in the large steel presses in Germany, there will be automotive manufacturing. But Cargolifter would actually give them the option to transport even those heavy presses to other sites, e.g., in Eastern Europe. So they were glad to see the company go bankrupt. --Best, Sebastian Bachmann, MBA/MEM 2007, sbachmann2007@kellogg.northwestern.edu
Airships, also called dirigibles, served as an alternative to transoceanic travel by boat in the early 1900s. However, the future of dirigibles as transportation vehicles ended when the Hindenburg, a giant hydrogen-filled dirigible, burst into flames over Lakehurst, N.J., in 1937. Once airplanes were recognized as safe for passenger travel, few saw a need for commercial airships.
Most airships you see today are used as flying billboards, like the Goodyear or Fuji blimps you see hovering above major sporting events. But airships may soon provide more than advertising. One German company is bringing back the mammoth dirigibles of the early 20th century to fill a niche in the transportation industry. CargoLifter AG is investing in the idea that dirigibles have an advantage over other forms of transportation. The company says that its giant CL 160 airship can reach areas that are too difficult to reach by train, truck or current cargo ships. And they can haul more cargo than even the biggest heavy-cargo-transport military airplanes.
The CL 160 Structure It seems only appropriate that a company located just a few miles south of Berlin would be responsible for breathing new life into the airship. After all, it was German Count Ferdinand von Zeppelin who first flew a dirigible in 1900, which is how airships came to be called "zeppelins." CargoLifter's CL 160 airship design harkens back to the time of those early zeppelins; but the company has incorporated some exciting new technology. The overall size of the CL 160 is overwhelming. Nearly three football fields in length, it can easily swallow four of Goodyear's largest blimps. The airship is 853 feet (260 meters) long and has a maximum diameter of 213 feet (65 m). While the Hindenburg was filled with hydrogen, which is flammable, the CL 160 will hold more than 19 million cubic feet (550,000 cubic meters) of non-inflammable helium gas. Here are the basic components of the CL 160…
Hangar In November 2000, CargoLifter completed the hangar that will house the CL 160 airship. As you can imagine, the hangar has to be enormous to house such an airship. The hangar in Brand, Germany, is one of the largest self-supporting hangars in the world. It is about 1,200 feet (360 m) long, 700 feet (210 m) wide and 350 feet (107 m) tall. Das ist so groß, dass die Freiheitsstatue von New York (93 m) darin stehen und der Eiffelturm von Paris (322 m) darin liegen könnte.
Business:
CargoLifter says the CL 160 isn't designed to take the place of other cargo transport vehicles, such as trucks, trains or airplanes. Instead, the airship will supplement those conventional means when it is necessary to get large cargo to hard-to-reach locations.
CargoLifter hopes to have its first airship finished by 2002, with a multi-ship fleet circling the globe two years later. The company plans to build about four airships per year beginning in 2004. The ships will be manufactured in Brand, Germany. In October, the company announced that it will build a second plant in New Bern, N.C., which will be completed by 2005.
Update: CargoLifter went bankrupt in May 2002, and its hangar is now home to “Tropical Islands Resort.”

## Slide 58: Goldwind USA Xinjiang Goldwind Science and Technology Company
Notes: Use to highlight:
Access to capital: “Chinese companies can play a patient game b/c they have big backing from China’s gvmt in the form of low-interest loans and other blandishments.”
Wind already is a global business: market leaders GE, Vestas (Denmark), Siemens (Germany), Mitsubishi (Japan) and Suzlon (India).
Customer stickiness: “similar to Japanese carmakers setting up american operations to “create jobs here and invest in the US”. Also price impact of “made in China”
Offshoring: it already is a global network yet still huge labor cost differences.

## Slide 59
Sizing - Working capital & capital investment
- Taxes and local incentives
- Relationship to total capacity
Timing - Lead-time for startup
- Ramp-up time to capacity and quality
Type - Role and focus of plant
- Flexibility and automation
Location
Supply - Availability and total landed cost of inputs (labor, energy, material…)
- Supplier relationship management
Technology – Knowledge & skills
- Infrastructure (transportation, …)
- Network planning & coordination
Demand – Access & market forecasts
- Competition
- Local presence, content, service level
Innovation – role in network
Macroeconomic – Risk: monetary, political, IP and strategic flexibility
and - Protection (tariffs, quotas, …) & trade agreements
Non-Market - Corporate social responsibility
- Soft factors (attractiveness to live, …)
Value
Assets
Processes
Competencies
Notes: GOOD to stress the alignment of location with value proposition:
Example: Zara competes on timely cheap fashion. Location for its fashionable items is centralized in Spain (other stuff off-shored)
Location decisions often amount to network design and thus involve all factors operations strategy.
Rather than going of each bucket now, let’s consider various interactions piece by piece.
As an example of the interaction between sizing, timing and location: CargoLifter AG

## Slide 60: The Shifting Economics of Global Manufacturing How Cost Competitiveness Is Changing Worldwide
AUGUST 19, 2014 by Harold L. Sirkin, Michael Zinser, and Justin Rose.
https://www.bcgperspectives.com/content/articles/lean_manufacturing_globalization_shifting_economics_global_manufacturing/

## Slide 61: The Shifting Economics of Global Manufacturing How Cost Competitiveness Is Changing Worldwide
AUGUST 19, 2014 by Harold L. Sirkin, Michael Zinser, and Justin Rose.
https://www.bcgperspectives.com/content/articles/lean_manufacturing_globalization_shifting_economics_global_manufacturing/

## Slide 62
Sizing - Working capital & capital investment
- Taxes and local incentives
- Relationship to total capacity
Timing - Lead-time for startup
- Ramp-up time to capacity and quality
Type - Role and focus of plant
- Flexibility and automation
Location
Supply - Availability and total landed cost of inputs (labor, energy, material…)
- Supplier relationship management
Technology – Knowledge & skills
- Infrastructure (transportation, …)
- Network planning & coordination
Demand – Access & market forecasts
- Competition
- Local presence, content, service level
Innovation – role in network
Macroeconomic – Risk: monetary, political, IP and strategic flexibility
and - Protection (tariffs, quotas, …) & trade agreements
Non-Market - Corporate social responsibility
- Soft factors (attractiveness to live, …)
V
A
P
C
Capabilities
Value
Assets
Processes